## Slide 1: EECE.4810/EECE.5730 Operating Systems
Instructor:
Dr. Michael Geiger
Spring 2017
Lecture 10:
Segmentation and paging

## Slide 2: Lecture outline
Announcements/reminders
  Poll posted to schedule midterm (on or near W 3/8)
    Please respond ASAP
  Project 1/HW 3 coming …
  HW 2 graded; to be returned Monday
    Cite sources (if you use them) and reword ideas
Today’s lecture
  Review: memory management
    Main memory
    Address translation basics
    Base and bounds
  Memory management
    Segmentation
    Paging

## Slide 3: Review: Address spaces
Multiprogrammed system—keep multiple processes resident in main memory
OS should provide
  Address independence: same numeric address used in multiple processes, kept logically distinct
  Protection: one process can’t access another’s address space unless explicitly given access
  Virtual memory: address space larger than physical memory
OS typically binds relocatable virtual addresses to physical address at execution time
  Requires dynamic address translation on every reference

## Slide 4: Review: Forms of address translation
Base and bounds
  Contiguous region allocated for entire address space
Segmentation
  Address space split into variable-sized segments
Paging
  Address space split into fixed-size pages
Tradeoffs between
  Flexibility (sharing, growth, VM)
  Size of data needed to support translation
  Speed of translation

## Slide 5: Review: Base and bounds
Each process allocated contiguous block for entire address space
Address space defined by two values
  Base (or relocation register): lowest PA used
  Bound (or limit): total size of address space
  Only OS can change values
  HW support: only two registers
Process sees virtual address space
0 ≤ address < bound
Simple translation: PA = VA + base

## Slide 6: Review: Base and Bounds

## Slide 7: Review: Base and bounds pros/cons
Pros
  Simple
  Fast (2 registers, adder, comparator)
  Context switch—save base/bound (mem if needed)
  Safe … as far as multiple processes are concerned
  Can relocate in physical memory without changing process
Cons
  Can’t keep program from accidentally overwriting its own code
  Can’t share (partial) code/data with other processes
  Can’t grow stack/heap as needed
  Fragmentation
Notes: Provides level of indirection: OS can move bits around behind the program's back, for instance, if program needs to grow beyond its bounds, or if need to coalesce fragments of memory. Stop program, copy bits, change base and bounds registers, restart.
Because OS manages the translation, we control the vertical, we control the horizontal.
Hardware cost:
2 registers
adder, comparator
Plus, slows down hardware because need to take time to do add/compare on every memory reference.
In 60's, thought to be too expensive!
But get better use of memory, and you get protection. These are really important. CPU speed (especially now) is the easy part.

## Slide 8: Review: Multiple-partition allocation
OS maintains variable-sized partitions for efficiency
Holes (blocks of available memory) scattered throughout memory; list maintained by OS
Memory allocated from list using:
  First-fit: allocate to first hole that’s big enough
  Best-fit: allocate to smallest hole that’s big enough
  Worst-fit: allocate to largest available hole

## Slide 9: Review: Fragmentation
Internal fragmentation
  Wasted space inside partition
External fragmentation
  Total memory space exists to satisfy request but is non-contiguous
  Result of leftover space as processes exit
  Can resolve through compaction
    Shuffle memory blocks to make partitions use consecutive addresses

## Slide 10: Segmentation
Base & bounds groups entire address space together
Programs more logically organized into units
  Main program, functions, stack, heap, etc.
Segment: contiguous region of memory
  Base & bounds = 1 segment
  Generalized segmentation allows >1 segment per program
Each process has a segment table
  Entry in table = segment
  HW support
    Segment table base register (STBR) points to segment table
    Segment table length register (STLR) indicates number of segments
Segment can be located anywhere in physical memory
  Each segment has: start, length, access permission
Processes can share segments
  Same start, length, same/different access permissions

## Slide 11: Segmentation
Notes: This should seem a bit strange: the virtual address space has gaps in it! Each segment gets mapped to contiguous locations in physical memory, but may be gaps between segments.
This is a little like walking around in the dark, and there are huge pits in the ground where you die if you step in the pit.
But! of course, a correct program will never step off into a pit, so ok.
A correct program will never address gaps; if it does, trap to kernel and then core dump. Minor exception: stack, heap can grow. In UNIX, sbrk() increases size of heap segment. For stack, just take fault, system automatically increases size of stack.
Detail: Protection mode in segmentation table entries. For example, code segment would be read-only (only execution and loads are allowed). Data and stack segment would be read-write (stores allowed).
What must be saved/restored on context switch? Typically, segment table stored in CPU, not in memory, because it’s small.
Contents must be saved/restored.

## Slide 12: Segment table
Segment # | V | Base | Bounds | Access | 
0 | 1 | 4000 | 700 | read/exec | code segment
1 | 1 | 0 | 500 | read/write | data segment
2 | 0 | n/a | n/a |  | unused segment
3 | 1 | 2000 | 1000 | read/write | stack segment
Protection handled by segment table contents
  Valid bit (V) indicates if segment in use
  Access indicates privileges (read/write/execute)
Virtual address: segment #, offset
  Segment number must be valid
  Offset must be < bound
  If either false, trap to OS  invalid address

## Slide 13: Segmentation
Pros?
  Can share code/data segments between processes
  Can protect code segment from being overwritten
  Can transparently grow stack/heap as needed
Cons?
  Complex memory management
    Need to find chunk of a particular size
  May need to rearrange memory from time to time to make room for new segment or growing segment
    External fragmentation: wasted space between chunks

## Slide 14: Segmentation example
Segment # | V | Base | Bounds | Access | 
0 | 1 | 219 | 600 | read/write | 
1 | 1 | 2300 | 14 | read/write | 
2 | 1 | 90 | 100 | read/exec | 
3 | 1 | 1327 | 580 | read/write | 
4 | 0 | 1952 | 96 | read | 
Given segment table above, what are physical addresses for following virtual addresses (of form <seg #>, <offset>)?
  0, 430
  1, 10
  2, 500
  3, 400
  4, 112

## Slide 15: Example solution
Segment # | V | Base | Bounds | Access | 
0 | 1 | 219 | 600 | read/write | 
1 | 1 | 2300 | 14 | read/write | 
2 | 1 | 90 | 100 | read/exec | 
3 | 1 | 1327 | 580 | read/write | 
4 | 0 | 1952 | 96 | read | 
Given segment table above, what are physical addresses for following virtual addresses (of form <seg #>, <offset>)?
  0, 430  219 + 430 = 649
  1, 10  2300 + 10 = 2310
  2, 500  offset > bound  illegal access
  3, 400  1327 + 400 = 1727
  4, 112  segment 4 not valid  illegal access

## Slide 16: Paged Translation
Manage memory in fixed size units, or pages
  Often refer to pages in virtual address space, frames in physical address space
Finding a free frame is easy
  Bitmap allocation: 0011111100000001100
  Each bit represents one physical page frame
Each process has its own page table
  Stored in physical memory
  Hardware registers
    pointer to page table start
    page table length
Notes: Simpler, because allows use of a bitmap. What's a bitmap?
001111100000001100
Each bit represents one page of physical memory -- 1 means allocated, 0 means unallocated. Lots simpler than base&bounds or segmentation

## Slide 17: Paged Translation (Abstract)

## Slide 18
Paged Translation (Implementation)

## Slide 19: Paging Questions
With paging, what is saved/restored on a process context switch?
  Pointer to page table, size of page table
  Page table itself is in main memory
What if page size is very small?
What if page size is very large?
  Internal fragmentation: if we don’t need all of the space inside a fixed size chunk
Notes: Means lots of space taken up with page table entries.

## Slide 20: Paging basics
Major benefits
  No need for bounds checking
  Easy to allocate fixed-size units
  Simple translation
    Virtual address: page number & offset
      Use page # to index into page table
    Physical address: frame number & offset
      Page # simply replaced by frame #--no arithmetic
Organization
  Usually one page size (some systems support >1)
    Page size determines offset size (log2(page size))
  VA > PA
    Larger virtual address space than physical address space
    # page table entries (PTE) determines page # size
    # frames determines frame # size

## Slide 21: Paging examples
Consider logical address space of 256 pages with 4 KB page size, mapped onto physical memory of 64 frames
  How many bits are in the virtual address?
  How many bits are in the physical address?
  What’s the total size of each address space (virtual and physical)?

## Slide 22: Paging examples
Consider logical address space of 256 pages with 4 KB page size, mapped onto phsyical memory of 64 frames
  Offset size = log2(4 KB) = log2(212 bytes) = 12 bits
  How many bits are in the virtual address?
    Page # size = log2(256 pages) = log2(28 pages) = 8 bits
    VA size = 8 + 12 = 20 bits
  How many bits are in the physical address?
    Frame # size = log2(64 frames) = log2(26 frames) = 6 bits
    VA size = 6 + 12 = 18 bits
  What’s the total size of each address space (virtual and physical)?
    Address space size = 2address size
    Virtual address space = 220 = 1 MB
    Physical address space = 218 = 256 KB

## Slide 23: Paging issues
What’s biggest issue with large virtual address space?
  Size of page table  space in memory, speed of translation
How do we determine page to evict if physical address space is full?

## Slide 24: Final notes
Next time: more on memory management
  Page table details
  Page table organizations (multilevel, inverted)
  Page replacement
Reminders:
  Poll posted to schedule midterm (on or near W 3/8)
    Please respond ASAP
  Project 1/HW 3 coming …
  HW 2 graded; to be returned Monday
    Cite sources (if you use them) and reword ideas

## Slide 25: Acknowledgements
These slides are adapted from the following sources:
  Silberschatz, Galvin, & Gagne, Operating Systems Concepts, 9th edition
  Anderson & Dahlin, Operating Systems: Principles and Practice, 2nd edition
  Chen & Madhyastha, EECS 482 lecture notes, University of Michigan, Fall 2016