## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 12:
Conditional execution

## Slide 2: Lecture outline
Announcements/reminders
  Exams to be returned Wednesday or Friday
  HW 4 to be posted; due date TBD
Today’s lecture
  Conditional execution

## Slide 3: Compare Instructions
Compare 2 values; store result in ZF/SF
General format: CMP D,S
  Works by performing subtraction (D) – (S)
    D, S unchanged
  ZF/SF/OF indicate result (signed values)
    ZF = 1  D == S
    ZF = 0, (SF XOR OF) = 1  D < S
    ZF = 0, (SF XOR OF) = 0  D > S
Notes: (D) (S) result CF SF AF
AX BX
2345>1234 0 0 0
1234<2345 1 1 1
1234>ABCD 1 0 1
ABCD<1234 0 1 0
ABCD>A000 0 0 0
A000<ABCD 1 1 1
7FFF 8000 overflow

## Slide 4: Condition codes
Conditional execution: result depends on value of flag bit(s)
Intel instructions specify condition codes
  Condition code implies certain flag values
  Opcodes written with cc as part of name
  cc can be replaced by any valid code
  Examples: CMOVcc, SETcc, Jcc
    Specific examples: CMOVE, SETL, SETZ, JNE, JG

## Slide 5: Condition codes (cont.)
Testing overflow
  O (OF = 1), NO (OF =0)
Testing carry flag
  C (CF = 1)
  NC (CF = 0)
Testing sign flag
  S (SF = 1), NS (SF = 0)
Testing parity flag
  P or PE (PF = 1)
  NP or PO (PF = 0)

## Slide 6: Condition codes (cont.)
Testing equality/zero result
  E or Z (ZF = 1)
  NE or NZ (ZF = 0)
Signed comparison
  L or NGE (SF XOR OF = 1)
  NL or GE (SF XOR OF = 0)
  LE or NG ((SF XOR OF) OR ZF = 1)
  NLE or G ((SF XOR OF) OR ZF = 0)
Unsigned comparison
  “Below”  less than, “above”  greater than
  B, NAE (CF = 1)
  NB, AE (CF = 0)
  BE or NA (CF OR ZF = 1)
  NBE or A (CF OR ZF = 0)

## Slide 7: Conditional move (CMOV)
Only in Pentium Pro & later
Perform move only if condition is true
Examples:
  CMOVZ AX, [SI]  move if ZF == 1
  CMOVG EBX, EAX  move if greater than

## Slide 8: Byte Set on Condition Instruction
Byte set on condition instruction
  Used to set byte based on condition code
  Can be used for boolean results—complex conditions
  General format:
    SETcc D
    cc = one of the supported conditional relationships
  Result
    D = 0x01 if condition true
    D = 0x00 if condition false

## Slide 9: Byte Set on Condition Instruction
Operation: Flags tested for conditions defined by “cc” and the destination in a register or memory updated as follows
If cc test True:
  000000012 = 0x01  D
  If cc test False:
  000000002 = 0x00  D
Examples of conditional tests:
SETE = set byte if equal  ZF = 1
SETC = set byte if carry  CF =1
SETBE = set byte if below or equal  CF = 1 +(or) ZF = 1
Example: SETA AL = set byte if above
  if CF = 0  (and) ZF = 0
  (AL) = 0x01
  Otherwise,
  (AL) = 0x00

## Slide 10: Example
Show the results of the following instructions, assuming that
  “A” = (0x100) = 0x0001
  “B” = (0x102) = 0x0003
  “C” = (0x104) = 0x1011
  “D” = (0x106) = 0x1011
  “E” = (0x108) = 0xABCD
  “F” = (0x10A) = 0xDCBA
What complex condition does this sequence test?
MOV AX, [0x100]
CMP AX, [0x102]
SETLE BL
MOV AX, [0x104]
CMP AX, [0x106]
SETE BH
AND BL, BH
MOV AX, [0x108]
CMP AX, [0x10A]
SETNE BH
OR BL, BH

## Slide 11: Example solution
Condition being tested:
  To simplify, treat each word as a variable named “A” through “F”
  ((A <= B) && (C == D)) || (E != F)
Source: http://www.arl.wustl.edu/~lockwood/class/cs306/books/artofasm/Chapter_6/CH06-4.html

## Slide 12: Jump instructions
Used to change flow of program
  Next instruction specified by operand
Two general types
  Unconditional: JMP <target>
    Always goes to address indicated by <target>
  Conditional: Jcc <target>
    Jump only occurs if condition true
    cc replaced by valid condition code
      Most codes discussed in previous lecture
      Additional codes: CXZ/ECXZ
       CX/ECX register is zero

## Slide 13: Final notes
Next time:
  Exams to be returned Wednesday or Friday
  Jump/loop instructions
Reminders:
  HW 4 to be posted; due date TBD