## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 5:
Assembly basics
Data transfer instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 1 due 2:00 PM today
  HW 2 to be posted; due 2:00 PM, Wednesday, 9/21
Today’s lecture
  Assembly basics
  Data transfer instructions

## Slide 3: Review: x86 data types
Refresher on x86 registers
  Gen. purpose registers: 16 or 32 bits
  Data registers can hold 8 bit data as well
  Determining size: register name
  Example: “accumulator” register
    8 bit data: AL = lowest byte; AH = next lowest byte
    16 bit data: AX = lowest 16 bits (AH/AL together as word)
    32 bit data: EAX = entire 32 bits
Say EAX = 0x1A2B3C4D
  What are AL, AH, and AX?
  AL = 4DH, AH = 3CH, AX = 3C4DH

## Slide 4: Review: x86 addressing modes
Addresses in x86 instructions enclosed by brackets
Addressing modes: all examples of general addressing modes discussed earlier
Direct addressing
  EA = constant value
  Example: MOV AX, [0x0100]
Register indirect addressing
  EA = value stored in register
  Example: MOV [EDI], AX
Base-plus-index addressing
  EA = sum of two registers
  Example: MOV AX, [EBX+ESI]

## Slide 5: Review: x86 addressing modes (cont.)
Register relative addressing
  EA = register + constant
  Examples:
    MOV CL, [EBX+4]
    MOV AX, ARRAY[EBX] ARRAY is constant memory location
Base relative-plus-index addressing
  EA = base register + index register + constant
  Example: MOV AX, 0x10[ESI][EBX] -or-
  MOV AX, [0x10+SI+BX]
Scaled-index addressing
  EA = register + (scaling factor * second register)
  Often useful for array accesses
    Scaling factor = element size (2, 4, 8 bytes)
  Example: MOV EDX, [EAX + 4*EBX]

## Slide 6: Example
Compute the address for the memory operand in each of the following instructions.
  You do not need to specify what data is transferred
The register contents and variables are as follows:
  (ESI) = 0x00000100
  (EDI) = 0x00000200
  (EBX) = 0x00000300
MOV [EBX+0x0400], CX
MOV [EDI+2*EBX], AH
MOV [EBX+EDI+0x0400], AL

## Slide 7: Example solutions
Memory operand in: MOV [EBX+0x0400], CX
  Addr = value in EBX + 0x0400
  = 0x00000300h + 0x0400 = 0x00000700
Memory operand in: MOV [EDI+2*EBX], AH
  Addr = value in EDI + 2 * value in EBX
  = 0x00000200 + 2 * 0x00000300
  = 0x00000200 + 0x00000600 = 0x00000800
Memory operand in MOV [EBX+EDI+0400h], AL
  Addr = EBX + EDI + 0x0400
  = 0x00000300 + 0x00000200 + 0x0400
  = 0x00000900

## Slide 8: Instruction Assembly Notation
Each instruction is represented by a mnemonic that describes its operation—called its operation code (opcode)
  MOV = move (data transfer)
  ADD = add (arithmetic)
  AND = logical AND (logic)
  JMP = unconditional jump (control transfer)
Operands are the other parts of an assembly language instructions
    Identify whether the elements of data to be processed are in registers or memory
      Source operand– location of one operand to be processed
      Destination operand—location of the other operand to be processed and the location of the result

## Slide 9: Assembly Language Statements
General structure of an assembly language statement
LABEL: INSTRUCTION ;COMMENT
  Label—address identifier for the statement
  Instruction—the operation to be performed
  Comment—documents the purpose of the statement
  Example:
START: MOV AX, BX ; Copy BX into AX
Other examples:
  INC SI ;Update pointer
ADD AX, BX
  Few instructions have a label—usually marks a jump to point
  Not all instructions need a comment

## Slide 10: x86 memory accesses
# bytes from memory usually = # bytes in register
Example: MOV AX, [0x100]
  AX is 16-bit register  copy word from address 0x100 to AX
Sometimes necessary to specify size
  Use “<size> PTR”: BYTE PTR, WORD PTR, DWORD PTR
  Example: MOVZX EAX, BYTE PTR [0x100]
    Take byte from memory
    Zero-extend data to 32 bits and store in EAX
Remember, x86 uses little-endian data

## Slide 11: Data transfer instructions
MOV
MOVSX
MOVZX
XCHG
LEA
Additional data transfer instructions (covered later, if at all)
  Load full pointer (segmented addressing)
  PUSH/POP (stack transfers)
  INS/OUTS (I/O)
  MOVS/LODS/STOS (string instructions)
  BSWAP (switch from little endian to big endian)
  XLAT (table lookup)
  CMOV (conditional move)

## Slide 12: MOV
Used to copy data between
  Registers
  Registers/memory
  Immediate value (source only) to register/memory
Format: MOV D, S
Operation: (D) = (S)
Immediate value can only be used as source

## Slide 13: MOV examples
Assume: AX = 0x0100, SI = 0x3000,
(0x100) = 0x00, (0x101) = 0xFF
MOV BL, AL
  BL = AL = 0x00
MOV DX, SI
  DX = SI = 0x3000
MOV CX, [0x100]
  CX = word starting at 0x100 = 0xFF00

## Slide 14: Usage of Move Instruction
Example—Initialization of internal registers with immediate data and address information
  What is the final state of all affected registers?
MOV AX, 0
MOV BX, AX
MOV CX, 0x0A
MOV DX, 0x100
MOV SI, 0x200
MOV DI, 0x300

## Slide 15: Usage of Move Instruction (soln)
MOV AX, 0  AX = 0x0000
MOV BX, AX  BX = AX = 0x0000
MOV CX, 0x0A  CX = 0x000A
MOV DX, 0x100  DX = 0x0100
MOV SI, 0x200  SI = 0x0200
MOV DI, 0x300  DI = 0x0300

## Slide 16: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 17: Final notes
Next time:
  Finish data transfer instructions
  Arithmetic instructions
Reminders:
  HW 1 due 1:00 PM today
  HW 2 to be posted; due 1:00 PM, Friday, 2/5