## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 6:
Data transfer instructions (cont.)

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due 2:00 PM, 9/21
Review
  Data transfer instructions (MOV, MOVSX, MOVZX)
Today’s lecture
  More data transfer instructions

## Slide 3: Review: data & data transfer instructions
x86 data accesses
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
  If segment reg. is destination, source must be register

## Slide 4: Review: MOVSX/MOVZX
Move and extend data (fill upper bits with 0/1)
  ZX  zero extend
  SX  sign extend  copy MSB of source
Format: MOVZX D, S
MOVSX D, S
Operation: lower bits of D = S
upper bits of D = 0 (MOVZX) or
upper bits of D = MSB of S (MOVSX)
Restrictions
  Only register/memory operands (no immediates)
  Source must contain fewer bits than destination
  If memory operand used, size must be specified

## Slide 5: MOVSX/MOVZX examples
Assume: AX = 0x0100, DX = 0x8100,
(0x100) = 0x00, (0x101) = 0xFF
What are the results of the following instructions?
MOVSX EBX, AX
MOVSX EBX, DX
MOVZX EBX, DX
MOVSX EBX, BYTE PTR [0x100]
MOVSX EBX, WORD PTR [0x100]

## Slide 6: MOVSX/MOVZX examples (soln)
Assume: AX = 0x0100, DX = 0x8100,
(0x100) = 0x00, (0x101) = 0xFF
What are the results of the following instructions?
MOVSX EBX, AX
  EBX = AX sign-extended = 0x00000100 (orig. value underlined)
MOVSX EBX, DX
  EBX = DX sign-extended = 0xFFFF8100
MOVZX EBX, DX
  EBX = DX zero-extended = 0x00008100
MOVSX EBX, BYTE PTR [0x100]
  EBX = byte at 0x100 sign-extended = 0x00000000
MOVSX EBX, WORD PTR [0x100]
  EBX = word at 0x100 sign-extended = 0xFFFFFF00

## Slide 7: XCHG
Swap contents of source and destination
Format: XCHG D, S
Operation: (D) = (S)
(S) = (D)
Restrictions:
  Memory operand can only be used as destination

## Slide 8: LEA
Perform effective address computation and store result in register
  This instruction looks like a memory access, but does not access memory
Format: LEA D, EA
Operation: D = EA
Example: LEA SI, [0x10 + DI]
  SI = 0x10 + DI

## Slide 9: Example
 | Lo |  |  | Hi
0x528000 | 50 | 88 | 31 | A3
0x528004 | B2 | FF | 0F | 7D
0x528008 | 07 | D0 | BE | 22
0x52800C | 11 | 96 | 00 | 14
Given the initial memory contents at left, show the results of the following instruction sequence:
MOV EAX, 0x528000
MOV EBX, [EAX+2]
XCHG BL, BH
LEA EDX, [EAX+8]
MOV ECX, [EDX-3]

## Slide 10: Solution
MOV EAX, 0x528000
EAX = 0x528000
MOV EBX, [EAX+2]
EBX = DWORD at 0x528002 = 0xFFB2A331
XCHG BL, BH
Swap BL and BH  EBX = 0xFFB231A3
LEA EDX, [EAX+8]
EDX = EAX+8 = 0x528008
MOV ECX, [EDX-3]
ECX = DWORD at 0x528005 = 0x077D0FFF

## Slide 11: Final notes
Next time:
  Arithmetic instructions
Reminders:
  HW 2 due 2:00 PM, 9/21