## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Fall 2016
Lecture 8:
Multiplication and division instructions
Logical instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due 2:00 PM today
  HW 3 to be posted; due 2:00 PM, Wednesday, 9/28
    No late submissions—solution to be posted that day
  Exam 1: Friday, 9/30
    Allowed calculator, one double-sided 8.5” x 11” note sheet
    Will be given list of instructions covered so far
Review
  Arithmetic instructions
Today’s lecture
  Multiplication and division

## Slide 3: Review: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 4: Review: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 5: Multiplication/division
Both signed and unsigned integer versions
Register A is always one of the sources
Destination always same; size-dependent
  Exception: signed multiplication does allow for slightly different operation
Easiest way to evaluate instructions: figure out decimal values of operands, do operation in decimal, then figure out binary/hex values of results

## Slide 6: MUL/IMUL
MUL S  unsigned multiplication
IMUL S  signed multiplication
Byte: (AX) = (AL) * (S)
Word: (DX,AX) = (AX) * (S)
Double-word: (EDX,EAX) = (EAX) * (S)
Only CF, OF updated
  If upper half of result = 0, CF & OF = 0
  Otherwise, CF & OF = 1

## Slide 7: DIV/IDIV
DIV S  unsigned division
IDIV S  signed division
Result split into quotient, remainder
Byte: (AL) = (AX) / (S)
(AH) = (AX) % (S)
Word: (AX) = (DX,AX) / (S)
(DX) = (DX,AX) % (S)
Dword: (EAX) = (EDX,EAX) / (S)
(EDX) = (EDX,EAX) % (S)
Special “convert” instructions used to sign-extend value in register A before division
Flags undefined
  Overflow causes exception

## Slide 8: Example
Given
  EAX = 0x00000005
  EBX = 0x0000FF02
What are the results of the following instructions? (Assume all instructions start with same values in registers above)
  MUL BL
  MUL BH
  IMUL BH
  DIV BL
  DIV BH
  IDIV BH

## Slide 9: Solution
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
MUL BL
  AX = AL * BL = 0x05 * 0x02 = 5 * 2 = 1010 = 0x000A
MUL BH
  Unsigned multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * 255 = 127510
  = 0x04FB
IMUL BH
  Signed multiplication
  AX = AL * BH = 0x05 * 0xFF = 5 * -1 = -510 = 0xFFFB

## Slide 10: Solution (continued)
Consider that BH = 0xFF = 1111 11112
  As unsigned value, 0xFF = 25510
  As signed value, 0xFF = -110
DIV BL
  AL = AX / BL = 0x0005 / 0x02 = 5 / 2 = 0x02
  AH = AX % BL = 0x0005 % 0x02 = 5 % 2 = 0x01
DIV BH
  Unsigned division
  AL = AX / BH = 0x0005 / 0xFF = 5 / 255 = 0x00
  AH = AX % BH = 0x0005 / 0xFF = 5 % 255 = 0x05
IDIV BH
  Signed division
  AL = AX / BH = 0x0005 / 0xFF = 5 / -1 = -5 = 0xFB
  AH = AX % BH = 0x0005 % 0xFF = 5 % -1 = 0x00

## Slide 11: Final notes
Next time:
  Logical and shift instructions
Reminders:
  HW 2 due 2:00 PM today
  HW 3 to be posted; due 2:00 PM, Wednesday, 9/28
    No late submissions—solution to be posted that day
  Exam 1: Friday, 9/30
    Allowed calculator, one double-sided 8.5” x 11” note sheet
    Will be given list of instructions covered so far