## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 10:
Rotate, bit test, and bit scan instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 3 due today at 1:00 PM
    No late submissions—solution to be posted later today
  Exam 1: Friday, 2/19
    Allowed calculator, one double-sided 8.5” x 11” note sheet
    Will be given list of instructions covered so far
Review
  Logical instructions
  Shift instructions
Today’s lecture
  Rotate instructions
  Bit test/scan instructions

## Slide 3: Review: Logical instructions
Logical instructions (AND/OR/XOR/NOT)
Basic shift instructions
  Move value by <amt> bits; add 0s to left or right
  CF = last bit shifted out
  SHL <src>, <amt>: Move <src> to left
    SAL exactly the same
  SHR <src>, <amt>: Move <src> to right
Arithmetic right shift
  Move value right by <amt> bits
  Copy sign bit to fill remaining bits
  CF = last bit shifted out
  SAR <src>, <amt>

## Slide 4: Rotate instructions
Difference between rotates and shifts
  Shifts discard bits that are shifted out
  Rotates take bits that are shifted out and use them to fill vacated bits
Rotate instruction format: <op> D, <shamt>
  Destination may be register/memory
  <shamt>: shift amount
    May be immediate or register CL
All rotate instructions store last bit shifted out in carry flag (CF)

## Slide 5: ROR / ROL / RCR / RCL
ROR: rotate right
  Shift (D) to right by <shamt> bits
  <shamt> LS bits are moved to MS bits
ROL: rotate left
  Shift (D) to left by <shamt> bits
  <shamt> MS bits are moved to LS bits
RCR: rotate right through carry
  Treat (CF) as extra LS bit
  Shift (D,CF) to right by <shamt> bits
  <shamt> LS bits (from (D,CF)) are moved to MS bits
RCL: rotate left through carry
  Treat (CF) as extra MS bit
  Shift (CF,D) to left by <shamt> bits
  <shamt> MS bits (from (CF,D)) are moved to LS bits

## Slide 6: ROL example
ROL AX,1
Before execution
  Dest = (AX) = 1234H = 0001 0010 0011 01002
  Count = 1, CF = 0
Operation
  The value in all bits of AX are rotated left one bit position
  Value rotated out of the MSB is reloaded at LSB
  Value rotated out of MSB copied to carry flag
After execution
  Dest = (AX) = 2468H = 00100100011010002
  CF = 0

## Slide 7: ROR example
ROR AX,CL
Before execution
  Dest = (AX) = 1234H = 0001 0010 0011 01002
  Count = 04H, CF = 0
Operation
  The value in all bits of AX are rotated right four bit positions
  Values rotated out of the LSB are reloaded at MSB
  Values rotated out of MSB copied to carry flag
After execution
  Dest = (AX) = 4123H = 01000001001000112
  CF = 0
Note position of hex characters in AX have been rearranged

## Slide 8: RCL example
RCL BX,CL
Before execution
  Dest = (BX) = 1234H = 0001 0010 0011 01002
  Count = 04H, CF = 0
Operation
  The value in all bits of AX are shifted left four bit positions
  Emptied MSBs are rotated through the carry bit back into the LSB
  Last value rotated out of MSB retained in carry flag
  First rotate loads prior value of CF at the LSB
After execution
  Dest = (BX) = 2340H = 0010 0011 0100 00002
  CF = 1

## Slide 9: Rotate example
Given AL = 43h, CL = 04h, and CF = 0, show the state of AL after each instruction in the sequence below:
  ROR AL, 2
  ROL AL, CL
  RCR AL, 3
  RCL AL, 4

## Slide 10: Solution
Initially, AL = 43h = 010000112
ROR AL, 2
  AL = 01000011 rotated right by 2
  = 11010000 = D0h
  CF = last bit rotated in = 1
ROL AL, CL
  AL = 11010000 rotated left by 4
  = 00001101 = 0Dh
  CF = last bit rotated in = 1

## Slide 11: Solution (cont.)
RCR AL, 3
  (AL,CF) = 00001101 1 rotated right by 3
  = 01100001 1
  CF = 1, AL = 011000012 = 61h
RCL AL, 4
  (CF,AL) = 1 01100001 rotated left by 4
  = 0 00011011
  CF = 0, AL = 000110112 = 1Bh

## Slide 12: Bit Test Instructions
BT  Bit test
BTR  Bit test and reset
BTS  Bit test and set
BTC  Bit test and complement
Format of bit test instruction: BT(x) D,S
  (S)  index that selects the position of the bit tested
  (D)  Holds value tested
Operation:
  Enables programmer to test bit in a value in register or memory
  All  Save the value of the selected bit in the CF
  BT  Leaves selected bit unchanged
  BTR  Clears the bit (bit = 0)
  BTS  Sets the bit (bit = 1)
  BTC  Complements the bit (bit = ~bit)

## Slide 13: Bit Test Instructions
Example:
  BTC BX,7
Before execution
  (BX) = 03F0H = 0000 0011 1111 00002
After Execution
  (CF) = bit 7 of BX = 1
  (BX) = 0370H = 0000 0011 0111 00002

## Slide 14: Bit Scan Instructions
BSF  Bit scan forward
BSR  Bit scan reverse
Format of bit scan instructions: BS(x) D,S
  (S)  Holds value for which bits are tested to be 0
  (D)  Index of first bit that tests as non-zero
Operation:
  Enable programmer to test value to determine if all bits are 0
  BSF  Scans bits starting from bit 0
    Set ZF = 0 if all bits are found to be zero
    Sets ZF = 1 when first 1 bit detected and places index of that bit into destination
  BSR  Scans bits starting from MSB
    Set ZF = 0 if all bits are found to be zero
    Sets ZF = 1 when first 1 bit detected and places index of that bit into destination
Example:
  BSF ESI,EDX  32-bits of EDX scanned starting from B0
  If EDX = 00000000  ZF = 0 (all bits zero)
  If EDX = 00000001  ESI = 00000000, ZF = 1 (bit 0 is 1)
  If EDX = 00003000  ESI = 0000000C, ZF = 1 (bit 12 is first bit set to 1)

## Slide 15: Example
Given initial state shown in handout
List all changed registers/memory locations and their values, as well as CF
Instructions
  BT WORD PTR [21102h], 4
  BTC WORD PTR [21110h], 1
  BTS WORD PTR [21104h], 1
  BSF CX, WORD PTR [2110Eh]
  BSR DX, WORD PTR [21109h]

## Slide 16: Example solution
BT WORD PTR [21102h], 4
  Word at 21102 = 1010h = 0001 0000 0001 0000
  CF = bit 4 = 1
BTC WORD PTR [21110h], 1
  Word at 21110 = 001Eh = 0000 0000 0001 1110
  CF = bit 1 = 1
  Complement bit 1
    Word at 21110 = 0000 0000 0001 1100 = 001Ch

## Slide 17: Example solution (cont.)
BTS WORD PTR [21104h], 1
  Word at 21104 = 0189h = 0000 0001 1000 1001
  CF = bit 1 = 0
  Set bit 1
    Word at 21110 = 0000 0001 1000 1011 = 018BH
BSF CX, WORD PTR [2110Eh]
  Word at 2110E = 00FFh = 0000 0000 1111 1111
  Word is not zero  ZF = 1
  First non-zero bit (starting from bit 0) is bit 0  CX = 0000h
BSR DX, WORD PTR [21109h]
  Word at 2110E = 0000h = 0000 0000 0000 0000
  Word is zero  ZF = 0
  DX unchanged

## Slide 18: Final notes
Next time:
  Exam 1 Preview
Reminders:
  HW 3 due today at 1:00 PM
    No late submissions—solution to be posted later today
  Exam 1: Friday, 2/19
    Allowed calculator, one double-sided 8.5” x 11” note sheet
    Will be given list of instructions covered so far