## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 14:
Subroutines

## Slide 2: Lecture outline
Announcements/reminders
  HW 4 to be posted; due date TBD (likely 3/4)
  Exams to be returned Monday
    Yes, I’m actually serious this time
Today’s lecture
  Subroutines
  Stack details

## Slide 3: Subroutines
Subroutine: special program segment that can be “called” from any point in program
  Implements HLL functions/procedures
  Written to perform operation that must be repeated in program
  Actual subroutine code only written once

## Slide 4: Subroutine operation
When called, address of next instruction saved
  State may need to be saved before call
  Parameters can be passed
Control of program transferred to subroutine
After subroutine finished, return instruction goes back to saved address

## Slide 5: x86 subroutines
Specify starting point with pseudo-op
  <name> PROC
May save state/allocate variables at start
  If so, will restore at end of subroutine
Last instruction returns to saved address
  Always RET
Pseudo-op after RET indicates routine end
  <name> ENDP

## Slide 6: Subroutine example
SQUARE PROC
PUSH AX ; Save AX to stack
MOV AL, BL ; Copy BL to AL
IMUL BL ; AX = BL * AL
; = original BL squared
MOV BX, AX ; Copy result to BX
POP AX ; Restore AX
RET
SQUARE ENDP

## Slide 7: Call/return
Calling subroutine: CALL <proc>
  Address of next instruction saved on stack
    Either IP or EIP (instruction pointer)
When function ends, use return instruction (RET)
  Jumps to saved return address (IP/EIP)

## Slide 8: Example
Assuming AX = 2 and BX = 4, show the results of the following sequence:
  Assume the addresses of the first three instructions are 0005, 0008, and 0009, respectively
  CALL SUM
  RET ; End main function
  SUM PROC NEAR
  MOV DX, AX
  ADD DX, BX
  RET
  SUM ENDP

## Slide 9: Example results
  CALL SUM
  RET ; End main function
  SUM PROC NEAR
  MOV DX, AX DX = AX = 2
  ADD DX, BX DX = DX + BX = 2 + 4 = 6
  RET
  SUM ENDP

## Slide 10: Saving state
May need to save state before routine starts
  Overwritten registers (that aren’t return values)
  Flags
Placing data on stack: PUSH
  Store data “above” current TOS; decrement SP
    Stack grows toward lower addresses
    New SP points to start of data just stored
  Basic PUSH stores word or double word
  Directly storing flags: PUSHF
  Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD

## Slide 12: Restoring state
Removing data from TOS: POP
  Data removed from TOS; SP incremented
  Basic POP removes word/double word
  Directly removing flags: POPF
  Removing all 16-/32-bit general purpose registers: POPA/POPAD
POP instructions generally executed in reverse order of corresponding PUSH instructions

## Slide 13: Revisiting subroutine example
SQUARE PROC NEAR
PUSH AX ; Save AX to stack
MOV AL, BL ; Copy BL to AL
IMUL BL ; AL = BL * AL
; = original BL squared
MOV BX, AX ; Copy result to BX
POP AX ; Restore AX
RET
SQUARE ENDP

## Slide 14: Push All and Pop All Operations

## Slide 15: Stack examples
Assume initial state shown in handout
What is the resulting stack state of each of the following sequences?
  PUSH BX
  PUSH AX
  PUSH EBX
  PUSH EAX
  PUSHA

## Slide 16: Solution
What is the resulting stack state of each of the following sequences?
  PUSH BX
  PUSH AX
  4 bytes pushed to stack, so SP decremented by 4  ESP = 00001FFCH
  AX is at top of stack; BX is below that
  PUSH EBX
  PUSH EAX
  8 bytes pushed to stack, so SP decremented by 8  ESP = 00001FF8H
  EAX is at top of stack; EBX is below that
  PUSHA
  8 words = 16 bytes pushed to stack, so SP decremented by 16  ESP = 00001FF0H
  As shown in slide 13, DI is at top of stack, followed by SI, BP, old SP, BX, DX, CX, and AX

## Slide 17: Final notes
Next time:
  Exam 1 Review (Monday)
  HLL  assembly (Wednesday)
Announcements/reminders
  HW 4 to be posted; due date TBD (likely 3/4)