## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 23
Exam 2 Preview

## Slide 2: Lecture outline
Announcements/reminders:
  HW 6 due 1:00 PM today—no late submissions accepted
Today’s lecture: Exam 2 Preview

## Slide 3: Exam 2 notes
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
No other notes or electronic devices (phone, laptop, etc.)
Exam will last 50 minutes
Covers lectures 12-14, 16-22
Format similar to previous exam
  1 multiple choice question
  2-3 short problems to solve/code sequences to evaluate

## Slide 4: Review: compare
CMP D, S
  Flags show result of (D) – (S)
Condition codes: mnemonics implying certain flag conditions

## Slide 5: Review: conditional instructions
Conditional move
  Move performed only if condition is true
SETcc D
  Sets single byte destination to 1 (01H) if condition true; all 0s (00H) if condition false
  Can be used to build up complex conditions

## Slide 6: Review: jump, loop
Two general types of jump
  Unconditional: JMP <target>
    Always go to target address
  Conditional: Jcc <target>
    Go to target address if condition true
Loop instructions
  Combines CX decrement with JNZ test
  May add additional required condition
    LOOPE/LOOPZ: loop if ((CX != 0) && (ZF == 1))
    LOOPNE/LOOPNZ: loop if (CX != 0) && (ZF == 0))

## Slide 7: Review: subroutines
Subroutines: low-level functions
  When called, address of next instruction saved
    Return instruction ends routine; goes to that point
  May need to save state on stack
x86 specifics
  CALL <proc>: call procedure
    <proc> can be label (16-/32-bit imm), reg, mem
  RET: return from procedure
  Saving state to stack: push instructions
    Store data “above” current TOS; decrement SP
    Basic PUSH stores word or double word
    Directly storing flags: PUSHF
    Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD
  Restoring state: POP/POPF/POPA/POPAD

## Slide 8: Review: HLL  assembly
Data accesses
  Global variables  static; allocated in data segment
  Other variables  dynamic; allocated on stack
  Stack frame for each function contains (from top)
    Saved variables within function
    Local variables for function (starting at EBP – 4)
    Saved EBP
    Saved EIP
    Function arguments (starting at EBP + 8)
Conditional statements (if-then-else)
  Evaluate condition (CMP instruction(s))
  Conditional jump (often to “else” case)
  “If” case ends with unconditional jump to skip “else”
Loops
  Initialize variable at start
  Test loop condition (similar to if)
  Change loop variable

## Slide 9: Review: PIC instructions
Four typical instruction formats (+ few special purpose)
  Upper bits of all hold opcode
  Byte-oriented includes 1 bit destination, 7 bit direct address
  Bit-oriented includes 3 bit position (0-7), 7 bit direct address
  Literal/control includes 8 bit literal
  CALL/GOTO includes 11 bit literal
Variable declarations
  cblock <start_address>: start of variable declarations
  All names between cblock/endc directives assigned to consecutive bytes starting at <start_address>

## Slide 12: Review: PIC instructions (cont.)
Clearing register: clrw/clrf
Moving values: movlw/movwf/movf
Swap nibbles: swapf
Single bit manipulation: bsf/bcf
Unary operations: incf/decf/comf
Arithmetic: addlw/addwf/addwfc/
sublw/subwf/subwfb

## Slide 13: Review: PIC instructions (cont.)
Logical operations
  andlw/andwf
  iorlw/iorwf
  xorlw/xorwf
Rotates/shifts
  rrf/lsrf/asrf
  rlf/lslf
Jumps/calls/return
  goto/bra
  call
  return/retlw/retfie
Conditional execution
  Test bit and skip next instruction if clear/set: btfsc/btfss
  Increment/decrement register and skip next instruction if zero: incfsz/decfsz
Example use: combined with goto to create conditional jump

## Slide 14: Final notes
Next time:
  Exam 2—PLEASE BE ON TIME
Reminders
  HW 6 due 1:00 PM today—no late submissions accepted