## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Spring 2016
Lecture 7:
Arithmetic instructions

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 due 1:00 PM, 2/5
  HW 3 to be posted; due 1:00 PM 2/12
Review
  Data transfer instructions (XCHG, LEA)
Today’s lecture
  Arithmetic instructions

## Slide 3: Review: XCHG, LEA
XCHG: swap contents of source, dest
  For example, given AX = 1234h and BX = 5678h:
  XCHG AX, BX  AX = 5678h, BX = 1234h
LEA: load effective address
  Store result of effective address computation in register
  Instruction doesn’t actually access memory
  For example, given AX = 3170h:
  LEA CX, [AX+0220h]  CX = 3390h

## Slide 4: Flags
All arithmetic instructions set flags
  CF = carry flag (carry output from MSB of add/sub)
  OF = overflow flag
  ZF = zero flag (result is zero)
  SF = sign flag (1 if negative, 0 if positive)
  PF = parity flag (even parity in LSB)
  AF = auxiliary carry (carry between nibbles)
Stored in FLAGS register
Referenced in conditional instructions

## Slide 5: Addition instructions
ADD D, S
  Operation: (D) = (D) + (S)
ADC D, S
  Operation: (D) = (D) + (S) + (CF)
INC D
  Operation: (D) = (D) + 1

## Slide 6: Subtraction instructions
SUB D, S
  Operation: (D) = (D) – (S)
SBB D, S
  Operation: (D) = (D) – (S) – (CF)
DEC D
  Operation: (D) = (D) – 1
NEG D
  Operation: (D) = -(D)
  Two’s complement negation

## Slide 7: Addition/subtraction examples
Given the following initial state:
  AX = 1234h
  BL = ABh
  Memory location SUM = 00CDh
Show the results of each step of the following instruction sequence:
  ADD AX, [SUM]
  ADC BL, 05h
  NEG BL
  SUB AX, 12h
  INC WORD PTR [SUM]

## Slide 8: Example solution
ADD AX, [SUM]
  (AX) = (SUM) + (AX)
  00CDh + 1234h = 1301h
  (AX) = 1301h, (CF) = 0
ADC BL, 05h
  (BL) = (BL) + 05h +(CF)
  ABh + 05h + 0 = B0h
  (BL) = B0h, (CF) = 0
NEG BL
  (BL) = –(BL)
  –B0h = –(1011 0000)2 = 0101 00002 = 50h

## Slide 9: Example solution (cont.)
SUB AX, 12h
  (AX) = (AX) – 0012h
  1301h – 0012h = 12EFh
  (AX) = 12EFh, (CF) = 0
INC WORD PTR [SUM]
  (SUM) = (SUM) + 1
  00CDh + 1 = 00CEh
  (SUM) = 00CEh, (CF) = 0

## Slide 10: Final notes
Next time:
  Multiplication and division
  Logical and shift instructions
Reminders:
  HW 2 due 1:00 PM, 2/5
  HW 3 to be posted; due 1:00 PM 2/12