## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2016
Lecture 11:
PIC assembly programming

## Slide 2: Lecture outline
Announcements/reminders
  HW 5 to be posted; due Monday, 6/20
  HW 6 to be posted; due Thursday, 6/23
    PICkit-based programming exercise
    Encouraged to work in groups (maximum of 3 students)
    Submissions received by 11:59 PM on Wednesday, 6/22 will earn an extra 10%
    Must return PICkit by end of exam on Thursday, 6/23
  Exam 3: Thursday, 6/23
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided
Today’s lecture
  Finish PIC instruction set (special-purpose instructions)
  Common simple operations
  Multi-byte data
  Short PIC programs

## Slide 3: Miscellaneous
Notes:
clrwdt ; if watchdog timer is enabled, this instruction will reset
; it (before it resets the CPU)
sleep ; Stop clock; reduce power; wait for watchdog timer or
; external signal to begin program execution again
nop ; Do nothing; wait one clock cycle
clrwdt ; clear watchdog timer
sleep ; go into standby mode
reset ; software reset
nop ; no operation
STATUS bits:
clrwwdt, sleep:
NOT_TO, NOT_PD
nop: none

## Slide 4: Working with multiple registers
Can’t do simple data transfer or operation on two registers
Usually must involve working register
Examples (assume X, Y file registers):
  X = Y
    movf Y, W
    movwf X
  X = X + Y
    movf Y, W
    addwf X, F

## Slide 5: Conditional jumps
Basic ones are combination of bit tests, skips
Remember that condition you’re testing is opposite of jump condition
Examples:
  Jump to label if carry == 0 (similar to x86 JNC)
    btfss STATUS, C
    goto label
  Jump if result of comparison is equal (~x86 JE)
    btfsc STATUS, Z
    goto label

## Slide 6: Conditional jumps (cont.)
To evaluate other conditions, may want to use subtraction in place of compare
Comparing X & Y turns into:
  movf Y, W
  subwf X, W
Possible results (unsigned comparison only):
  X > Y  Z = 0, C = 1
  X == Y  Z = 1, C = 1
  X < Y  Z = 0, C = 0
More complex conditions
  X <= Y  Z == C
  X != Y  Z = 0
  X >= Y  C = 1

## Slide 7: Shift/rotate operations
May need to account for bit being shifted/rotated out
  Basic rotate doesn’t rotate through carry
  Can either pre-test or fix later
Multi-bit shift/rotate: loop where # iterations matches shift amount

## Slide 8: Shift/rotate operations (cont.)
Examples:
  Rotate X to the right by 1 without the carry
    bcf STATUS, C ; Clear carry bit
    rrf X, F ; Rotate X one bit to right
    btfsc STATUS, C ; Skip next instruction if C clear
    ; C = bit shifted out of MSB
    bsf X, 7 ; Handle case where C = 1
    ; MSB of X should be 1
  Rotate X through the carry to the left by 3
    movlw 3 ; Initialize working register to 3 (# iterations)
    movwf COUNT ; Initialize count register
    ; Assumes you’ve declared variable COUNT
    Loop: rlf X, F ; Rotate Xone bit to left
    decfsz COUNT, F ; Decrement counter & test for 0
    ; Skip goto if result is zero
    goto Loop ; Return to start to loop

## Slide 9: Examples
Translate these x86 operations to PIC code
Assume that there are registers defined for each x86 register (e.g. AL, AH, BL, BH, etc.)
  Note: there is no actual translation from x86 to PIC
OR AL, BL
SUB BL, AL
JNZ label
JB label (B = below = unsigned <)
ROL AL, 5

## Slide 10: Example solution
OR AL, BL
  movf BL, W ; W = BL
  iorwf AL, F ; AL = AL OR W = AL OR BL
SUB BL, AL
  movf AL, W ; W = AL
  subwf BL, F ; BL = BL – W = BL – AL
JNZ label
  btfss STATUS, Z ; Skip goto if Z == 1 (if
  goto label ; previous result == 0)

## Slide 11: Example solution (continued)
JB label
  btfsc STATUS, Z ; If Z == 0, check C
  goto End ; Otherwise, no jump
  btfss STATUS, C ; If C == 1, no jump
  goto label ; Jump to label
  End: ; End of jump

## Slide 12: Example solution (continued)
ROL AL, 5
  movlw 5 ; W = 5
  movwf COUNT ; COUNT = W = 5
  L: bcf STATUS, C ; C = 0
  btfsc AL, 7 ; Skip if MSB == 0
  bsf STATUS, C ; C = 1 if MSB == 1
  ; C will hold copy of
  ; MSB (bit rotated into
  ; LSB)
  rlf AL, F ; Rotate left by 1
  decfsz COUNT ; If COUNT == 0, don’t
  ; restart loop
  goto L

## Slide 13: Multi-byte data
Logical operations can be done byte-by-byte
Arithmetic and shift/rotate operations require you to account for data flow between bytes
  Carry/borrow in arithmetic
  Bit shifted between bytes in shift/rotate
Order of these operations is important
  Arithmetic: must do least significant bytes first
  Shift/rotate: move through bytes in same order as shift  bits being shifted will move through carry
    Initial instruction should be appropriate operation (shift or rotate)
    All other instructions must be rotate operations

## Slide 14: Working with 16-bit data
Assume a 16-bit counter, the upper byte of the counter is called COUNTH and the lower byte is called COUNTL.
Decrement a 16-bit counter
movf COUNTL, F ; Set Z if lower byte == 0
btfsc STATUS, Z
decf COUNTH, F ; if so, decrement COUNTH
decf COUNTL, F ; in either case decrement COUNTL
Test a 16-bit variable for zero
movf COUNTL, F ; Set Z if lower byte == 0
btfsc STATUS, Z ; If not, then done testing
movf COUNTH, F ; Set Z if upper byte == 0
btfsc STATUS, Z ; if not, then done
goto BothZero ; branch if 16-bit variable == 0
CarryOn

## Slide 15: Examples
Translate these x86 operations to PIC code
Assume that there are registers defined for each x86 register (e.g. AL, AH, BL, BH, etc.)
  16-bit values (e.g., AX) must be dealt with as individual bytes
MOVZX AX, BL
MOVSX AX, BL
INC AX
SUB BX, AX
RCL AX, 5

## Slide 16: Example solutions
MOVZX AX, BL
movf BL, W ; Copy BL to W
movwf AL ; Copy W to AL
clrf AH ; Clear upper byte
MOVSX AX, BL
movf BL, W ; Copy BL to W
movwf AL ; Copy W to AL
clrf AH ; Clear upper byte
btfsc AL, 7 ; Test sign bit
decf AH, F ; If sign bit = 1, set
; AH = 00 - 1 = 0xFF

## Slide 17: Example solutions
INC AX
incf AL, F ; Increment low byte
btfsc STATUS, Z ; Check zero bit
incf AH, F ; If Z == 1, increment
; high byte
SUB BX, AX
movf AL, W ; Copy AL to W
subwf BL, F ; BL = BL – AL
movf AH, W ; Copy AH to W
subwfb BH, F ; BH = BH - AH

## Slide 18: Example solutions
RCL AX, 5
movlw 5 ; W = 5
movwf COUNT ; COUNT = W = 5
; Assumes register
; COUNT is defined
L: rlf AL, F ; Rotate low byte
; Bit transferred from
; low to high byte is
; now in carry
rlf AH, F ; Rotate high byte
decfsz COUNT, F ; Decrement & test COUNT
goto L ; Return to start of loop if
; COUNT != 0

## Slide 19: A Delay Subroutine
; ***********************************************************************************
; TenMs subroutine and its call inserts a delay of exactly ten milliseconds
; into the execution of code.
; It assumes a 4 MHz crystal clock. One instruction cycle = 4 * Tosc.
; TenMsH equ 13 ; Initial value of TenMs Subroutine's counter
; TenMsL equ 250
; COUNTH and COUNTL are two variables
TenMs
nop ; one cycle
movlw TenMsH ; Initialize COUNT
movwf COUNTH
movlw TenMsL
movwf COUNTL
Ten_1
decfsz COUNTL,F ; Inner loop
goto Ten_1
decfsz COUNTH,F ; Outer loop
goto Ten_1
return

## Slide 20: Delay subroutine questions
What factors determine amount of delay?
  Clock period (1/frequency)
  Clock cycles per instruction
  Number of instructions in loop
  Initial values of counter (COUNTL/COUNTH)
    TenMsH/TenMsL: constants used to initialize counter
What’s downside of using loop for delay?
  Processor does nothing but wait
Under what conditions does this function decrement the upper byte (COUNTH)?
  When COUNTL == 0
    First decfsz skips goto
    Second decfsz changes COUNTH

## Slide 21: Delay subroutine questions (cont.)
Under what conditions does function return?
  COUNTL == COUNTH == 0
How many times does each instruction execute?
  Everything before Ten_1 label: 1 time
  First decfsz/goto pair: depends on loop iteration
    First iteration: decfsz  250 times, goto  249 times
      goto skipped in last iteration
    All others: decfsz  256 times, goto  255 times
      Start by decrementing 0x00  0xFF (255)
  Second decfsz/goto pair: decfsz 13 times, goto 12 times
  return instruction: 1 time

## Slide 22: Blinking LED example
Assume three LEDs (Green, Yellow, Red) are attached to Port D bit 0, 1 and 2. Write a program for the PIC16F874 that toggles the three LEDs every half second in sequence: green, yellow, red, green, ….
For this example, assume that the system clock is 4MHz.

## Slide 23: Top Level Flowchart
Initialize: Initialize port D, initialize the counter for 500ms.
Blink: Toggle the LED in sequence, green, yellow, red, green, …. Which LED to be toggled is determined by the previous state.
Wait for 500ms: Keep the LED on for 500ms and then toggle the next one.

## Slide 24: Strategy to “Blink”
The LEDs are toggled in sequence - green, yellow, red, green, yellow, red…
Let’s look at the lower three bits of PORTD
  001=green, 010=yellow, 100=red
The next LED to be toggled is determined by the current LED.
001->010->100->001->…

## Slide 25: Inefficient “Blink” Subroutine
Blink
btfsc PORTD, 0 ; is it Green?
goto toggle1 ; yes, goto toggle1
btfsc PORTD, 1 ; else is it Yellow?
goto toggle2 ; yes, goto toggle2
;toggle0
bcf PORTD, 2 ; otherwise, must be red, change to green
bsf PORTD, 0 ; 100->001
return
toggle1
bcf PORTD, 0 ; change from green to yellow
bsf PORTD, 1 ; 001->010
return
toggle2
bcf PORTD, 1 ; change from yellow to red
bsf PORTD, 2 ; 010->100
return

## Slide 26: Inefficient “Blink” Subroutine Questions
Under what conditions will this function jump to “toggle1”?
  Lowest bit of PORTD = 1 (001, 011, 111)
Under what conditions will this function jump to “toggle2”?
  Lowest bit of PORTD = 0; second bit = 1 (010, 110)
If function gets into error state, how does it take to recover to valid state (only 1 bit == 1)?
  Depends on error state—1 or 2 function calls
Is there another way to toggle bits when changing state?
  What logical operation lets you toggle bits?
    XOR (1s in positions to change; 0s elsewhere)

## Slide 27: Another way to code “Blink” ---- Table Use
BlinkTable
movf PORTD, W ; Copy present state of LEDs into W
andlw B'00000111' ; and keep only LED bits
addwf PCL,F ; Change PC with PCL and offset in W
retlw B'00000001' ; (000 -> 001) reinitialize to green
retlw B'00000011' ; (001 -> 010) green to yellow
retlw B'00000110' ; (010 -> 100) yellow to red
retlw B'00000010' ; (011 -> 001) reinitialize to green
retlw B'00000101' ; (100 -> 001) red to green
retlw B'00000100' ; (101 -> 001) reinitialize to green
retlw B'00000111' ; (110 -> 001) reinitialize to green
retlw B'00000110' ; (111 -> 001) reinitialize to green
In calling program
call BlinkTable ; get bits to change into W
xorwf PORTD, F ; toggle them into PORTD

## Slide 28: Table Use Questions
What do the first two instructions do?
  Isolate lowest 3 bits of PORTD
  Ensure value in W is between 0-7
What does the addwf instruction do?
  Adding to PCL  effectively goto instruction
  Value in W = offset from addwf instruction
    If W = 0, add 0 to PCL  “jumps” to next instruction
    If W = 1, add 1 to PCL  “jumps” 1 extra instruction
    …
    If W = 7, add 7 to PCL  “jumps” 7 extra instructions
Why do we need 8 retlw instructions?
  8 possible values for lowest bits of PORTD
  8 possible states—3 valid ones (001, 010, 100) and 5 error states

## Slide 29: Table Use Questions (continued)
How is each return value used?
  Bit mask used in xorwf instruction
  Accomplishes appropriate state transition
  Valid states go through desired pattern
    001 XOR 011 = 010
    010 XOR 110 = 100
    100 XOR 101 = 001
  All error states transition back to 001
Why are upper 5 bits of return values = 0?
  May have other devices hooked up to port—don’t want to change state of those devices
  0 XOR 0 = 0; 1 XOR 0 = 1  XOR with 0 doesn’t change bit

## Slide 30: Final notes
Next time:
  PICkit basics
  Working with delay
Reminders:
  HW 5 to be posted; due Monday, 6/20
  HW 6 to be posted; due Thursday, 6/23
    PICkit-based programming exercise
    Encouraged to work in groups (maximum of 3 students)
    Submissions received by 11:59 PM on Wednesday, 6/22 will earn an extra 10%
    Must return PICkit by end of exam on Thursday, 6/23
  Exam 3: Thursday, 6/23
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided