## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2016
Lecture 12:
PICkit introduction
Working with delay

## Slide 2: Lecture outline
Announcements/reminders
  HW 5 to be posted; due Monday, 6/20
  HW 6 to be posted; due Thursday, 6/23
    PICkit-based programming exercise
    Encouraged to work in groups (maximum of 3 students)
    Submissions received by 11:59 PM on Wednesday, 6/22 will earn an extra 10%
    Must return PICkit by end of exam on Thursday, 6/23
  Exam 3: Thursday, 6/23
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided
Review
  Sample programming sequences: delay, state machine
Today’s lecture: working with PICkit
  Assembler directives
  MPLAB IDE
  Sample programs in assembly and C

## Slide 3: Review: complex operations
Multiple registers
  Data must be transferred through working register
Conditional jumps
  Usually btfsc/btfss instruction + goto
  Equality/inequality—use subtract in place of CMP
  If you subtract X – Y:
    X > Y  Z = 0, C = 1
    X == Y  Z = 1, C = 1
    X < Y  Z = 0, C = 0
    X <= Y  Z == C
    X != Y  Z = 0
    X >= Y  C = 1
Shift/rotate
  Manipulate carry before operation (or appropriate bit after)
  Use loop for multi-bit shift/rotate

## Slide 4: Review: Multi-byte data
Logical operations can be done byte-by-byte
Arithmetic and shift/rotate operations require you to account for data flow between bytes
  Carry/borrow in arithmetic
    Addition: if carry from lower byte, increment one of the upper bytes (addwfc)
    Subtraction: if borrow from lower byte, decrement one of the upper bytes (subwfb)
  Bit shifted between bytes in shift/rotate
    Performing instructions in correct order ensures bit transferred correctly through C bit
    All instructions after first one must be rrf/rlf
    Rotate/shift left: start with LSB
    Rotate/shift right: start with MSB

## Slide 5: Review: A Delay Subroutine
; ***********************************************************************************
; TenMs subroutine and its call inserts a delay of exactly ten milliseconds
; into the execution of code.
; It assumes a 4 MHz crystal clock. One instruction cycle = 4 * Tosc.
; TenMsH equ 13 ; Initial value of TenMs Subroutine's counter
; TenMsL equ 250
; COUNTH and COUNTL are two variables
TenMs
nop ; one cycle
movlw TenMsH ; Initialize COUNT
movwf COUNTH
movlw TenMsL
movwf COUNTL
Ten_1
decfsz COUNTL,F ; Inner loop
goto Ten_1
decfsz COUNTH,F ; Outer loop
goto Ten_1
return

## Slide 6: Review: Strategy to “Blink”
The LEDs are toggled in sequence - green, yellow, red, green, yellow, red…
Let’s look at the lower three bits of PORTD
  001=green, 010=yellow, 100=red
The next LED to be toggled is determined by the current LED.
001->010->100->001->…

## Slide 7: Review: Coding “Blink” with Table Use
BlinkTable
movf PORTD, W ; Copy present state of LEDs into W
andlw B'00000111' ; and keep only LED bits
addwf PCL,F ; Change PC with PCLATH and offset in W
retlw B'00000001' ; (000 -> 001) reinitialize to green
retlw B'00000011' ; (001 -> 010) green to yellow
retlw B'00000110' ; (010 -> 100) yellow to red
retlw B'00000010' ; (011 -> 001) reinitialize to green
retlw B'00000101' ; (100 -> 001) red to green
retlw B'00000100' ; (101 -> 001) reinitialize to green
retlw B'00000111' ; (110 -> 001) reinitialize to green
retlw B'00000110' ; (111 -> 001) reinitialize to green
In calling program
call BlinkTable ; get bits to change into W
xorwf PORTD, F ; toggle them into PORTD

## Slide 8: PIC microcontroller programming
Done through MPLAB IDE
Allows for generation of projects in assembly or in C
Options to generate initialization code
In-circuit debugger to view device state while hardware is actually running

## Slide 9: PIC assembler directives
banksel label
  Changes BSR to bank containing label
  Example: banksel TRISC
cblock/endc
  Used to define a block of variables
org address
  Indicates starting address for block of code that follows
  Address 0 in simple programs (initial PC value)
#include file
  Typically used to include processor-specific definitions, macros

## Slide 10: Example 1: Light single LED (.asm)
Start:
banksel TRISC ;select bank1
bcf TRISC,0 ;make C0 an output
banksel LATC ;select bank2
clrf LATC ;initialize the
; LATCH by
; turning off
; everything
bsf LATC,0 ;turn on LED C0 (DS1)
goto $ ;sit here forever!
end

## Slide 11: Example 1 notes (.asm)
TRISC: controls state of Port C pins
  TRISC bits = 1  corresponding pins are inputs
  TRISC bits = 0  corresponding pins are outputs
LATC: used for writing data to Port C
  Equivalent to writing to PORTC register
  Convention: for input, read PORTC; for output, write LATC
Infinite loop at end
  $ symbol—special label for current instruction

## Slide 12: Example 1: Light single LED (C)
void main(void) {
TRISCbits.TRISC0 = 0; // Pin 0 =
// output
LATC = 0; //clear all pins to 0
LATCbits.LATC0 = 1; // turn ON LED
while(1) continue;
}

## Slide 13: Example 1 notes (C)
Can access entire registers by name
To access individual bits, use form:
regnamebits.regname#
  Example: TRISCbits.TRISC0 = 0;

## Slide 14: Running program
Choose target device under
File  Project Properties
  Either use PICkit3 or Simulator
Compilation
  Clean and Build
  Make and Program Device (PICkit3 only)
    Separate options required for debug configuration
    Click arrow on right of button to build/make for debug
Window  PIC Memory Views
  Allows you to view file registers and/or SFRs

## Slide 15: Example: Blink LED (.asm) (1 of 2)
cblock 0x70 ;shared memory accessible from all banks
Delay1 ;Two registers for delay loop in shared mem
Delay2
endc
ORG 0
Start:
banksel OSCCON ;bank1
movlw b'00111000' ;set cpu speed of 500KHz
movwf OSCCON ;OSCCON configures
; internal clock
bcf TRISC,0 ;Pin C0 = output for DS1
banksel LATC ;bank2
clrf LATC ;Turn off all of the LEDs

## Slide 16: Example 2: Blink LED (.asm) (2 of 2)
MainLoop:
bsf LATC, 0 ;turn on DS1
OndelayLoop:
decfsz Delay1,f ;Waste time.
bra OndelayLoop ;Inner loop takes 3 instructions
; per loop * 256 loops = 768 instructions
decfsz Delay2,f ;The outer loop takes an additional 3
; instructions per loopp * 256 loops
bra OndelayLoop ;(768+3) * 256 = 197376 instructions /
; 125K instructions per second =
; 1.579 sec.
bcf LATC,0 ;Turn off LED C0
OffDelayLoop:
decfsz Delay1,f ;same delay as above
bra OffDelayLoop
decfsz Delay2,f
bra OffDelayLoop
bra MainLoop ;Do it again...
end

## Slide 17: Example 2: Blink LED (C)
void main(void) {
unsigned int delay; // 16 bit variable
OSCCON = 0b00111000; //500KHz clock speed
TRISCbits.TRISC0 = 0; //using pin as output
delay = 11250;
while (1) {
//each instruction is 8us (1/(500KHz/4))
while(delay-- != 0)continue;
LATCbits.LATC0 ^= 1; //toggle LED
delay = 11250; //reset delay counter
}
}

## Slide 18: Oscillator module
Configurable oscillators to determine controller speed
Internal or external oscillator
Multiple scalable internal clocks
  Low frequency: 31 kHz
  Medium frequency: 500 kHz
  High frequency: 16 MHz
    Generated from medium frequency
  Low and medium can be divided to produce frequencies from 16 MHz to 31.25 kHz
Clock selected using appropriate bits in OSCCON register

## Slide 19: “Simplified diagram” of clock sources

## Slide 20: Rotate LEDs with delay loop (asm)
Start:
banksel OSCCON ;bank1
movlw b'00111000' ;set cpu clock speed of 500KHz
movwf OSCCON
clrf TRISC ;make all of PORTC an output
banksel LATC ;select the bank where LATC is (bank2)
movlw b'00001000' ;start the rotation by setting DS4 ON
movwf LATC
MainLoop:
OndelayLoop:
decfsz Delay1,f ;Delay loop ~ 1.5 s
goto OndelayLoop
decfsz Delay2,f
goto OndelayLoop
Rotate:
lsrf LATC,F ;shift LEDs & turn on LED to the right
btfsc STATUS,C ;Is carry 1? (was DS1 just lit?)
bsf LATC, 3 ;if so, start the sequence over again
goto MainLoop
end ;end code section

## Slide 21: Rotate LEDs with delay loop (C)
void main(void) {
TRISC = 0; //all pins are outputs
OSCCON = 0b00111000; //500KHz clock speed
LATC = 0b0001000; //start rotation by setting
//DS4 ON - rotate from the right to left
while (1) {
__delay_ms(500); //delay 500ms
LATC >> = 1; //shift to the right by 1
// When last LED is lit, restart pattern
if(STATUSbits.C)
LATCbits.LATC3 = 1;
}
}

## Slide 22: Timer module
Internal timers common in microcontrollers
Used to generate delays, measure time between events, or count event occurrences
Typical interrupts for
  Timer overflow (common for generating delay)
  Timer compare (also for generating delay—stop when timer reaches certain value)
  Capture (what value does timer have when event occurs?)
Typical timer configurations
  Run at particular speed relative to system clock (prescaled)
  Increment every time external event occurs
PIC 16F1829 has 5 timers (four 8 bit, one 16 bit)

## Slide 23: Rotate with timer-based delay (asm) (1/2)
Start:
;Setup main init
banksel OSCCON ;bank1
movlw b'00111000’ ;set cpu clock speed to 500KHz
movwf OSCCON
;Configure the LEDs
banksel TRISC ;bank1
clrf TRISC ;make all of PORTC an output
banksel LATC ;bank2
movlw b'00001000‘ ;start with DS4 lit
movwf LATC
;Setup Timer0
banksel OPTION_REG ;bank1
;1:256 prescaler for a delay of:
; (insruction-cycle * 256-counts)*prescaler =
; ((8uS * 256)*256) =~ 524mS
movlw b'00000111’
movwf OPTION_REG

## Slide 24: Rotate with timer-based delay (asm) (2/2)
MainLoop:
btfss INTCON, TMR0IF ;did TMR0 roll over yet?
bra $-1 ;wait until TMR0 overflows
bcf INTCON, TMR0IF ;clear flag in software
;rotate the LEDs
banksel LATC ;bank2
lsrf LATC, f
btfsc STATUS,C ;did bit rotate into carry?
bsf LATC,3 ;yes, light DS4 back up
bra MainLoop ;continue forever
end

## Slide 25: Rotate with timer-based delay (C)
void main(void) {
OSCCON = 0b00111000; //500KHz clock speed
TRISC = 0; //all LED pins are outputs
LATC = 0;
//1:256 prescaler for a delay of: (instruction-cycle * 256
// counts)*prescaler = ((8uS * 256)*256) =~ 524mS
OPTION_REG = 0b00000111;
LATCbits.LATC4 = 1; //start with DS4 lit
while (1) {
//PIC can do work here, but this program just waits for flag
while (!INTCONbits.TMR0IF) continue;
INTCONbits.T0IF = 0; //flag MUST be cleared in software
LATC >> = 1; //rotate the LEDs
if (STATUSbits.C) //when last LED is lit, restart pattern
LATCbits.LATC3 = 1;
}
}

## Slide 26: Final notes
Next time:
  Interrupts
  Analog to digital conversion
Reminders:
  HW 5 to be posted; due Monday, 6/20
  HW 6 to be posted; due Thursday, 6/23
    PICkit-based programming exercise
    Encouraged to work in groups (maximum of 3 students)
    Submissions received by 11:59 PM on Wednesday, 6/22 will earn an extra 10%
    Must return PICkit by end of exam on Thursday, 6/23
  Exam 3: Thursday, 6/23
    Will again be allowed one 8.5” x 11” note sheet, calculator
    Instruction list to be provided