## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 11:
Exam 1 Preview

## Slide 2: Lecture outline
Announcements/reminders
  HW 2 solution to be posted later today
  Exam 1: Monday, 9/30
    Will be allowed calculator, one 8.5” x 11” double-sided note sheet
    x86 instructions covered through Wednesday are posted
Today’s lecture: Exam 1 Preview
  General exam notes
  Review of material

## Slide 3: Exam 1 notes
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
x86 instruction set (so far) provided for you
No other notes or electronic devices (phone, laptop, etc.)
Exam will be 50 minutes
  Will start at 8:00 or 11:00 AM—please be on time!
Covers all lectures through Wednesday, 9/25
General format
  1 multiple choice question
  2-3 short answer questions
  1 extra credit problem

## Slide 4: Test policies
Prior to passing out exam, I will verify that you only have one note sheet
  If you have multiple sheets, I will take all notes
You will not be allowed to remove anything from your bag after that point in time
  If you need an additional pencil, eraser, or piece of scrap paper during the exam, ask me
Only one person will be allowed to use the bathroom at a time
  You must leave your cell phone either with me or clearly visible on the table near your seat

## Slide 5: Review: base conversions
Binary  decimal: each digit has weight (1, 2, 4, 8, etc)
  Starting from rightmost bit = bit 0, nth bit has weight 2n
  To get magnitude, add weights of bits = 1
    e.g. 001001012 = 32 + 4 + 1 = 3710
Unsigned values: strictly non-negative (0 or positive)
  Most significant bit (MSB) represents highest weight
Signed values: can be positive or negative
  MSB represents sign: 0 = positive, 1 = negative
  To find magnitude of negative number, take 2’s complement
    e.g. 111101012 as signed value  2’s complement = 000010112 = 1110  111101012 = -1110
Hexadecimal: each digit represents four-bit sequence
  For example, 0x7 = 01112, 0xE = 11102
  If converting to decimal, multiply nth digit by 16n
    0x1E = 1 * 16 + 14 * 1 = 3010

## Slide 6: Review: ISA, storage
Instruction set architecture (cont.)
  Operands: the data being operated on
    How are the bits interpreted? (int, FP, signed/unsigned)
    What size are they? (byte, word, etc.)
    How do we reference operands?
Data storage
  Registers
    Small, fast set of on-chip storage (primarily for speed)
    Referenced by name
  Memory
    Larger, slower set of storage (primarily for capacity)
    Organized as hierarchy …
    … but programmer references single range of addresses
    Memory issues
      Aligned data: address divisible by number of bytes
      Endianness: 80x86 data is little endian

## Slide 7: Review: data & data transfer instructions
x86 data
  Registers: access as 8-bit (e.g. AL, AH), 16-bit (AX), 32-bit (EAX)
  Memory
    Data size usually matches register
    If not, explicitly specify (BYTE PTR, WORD PTR, DWORD PTR)
MOV: basic data transfer
  Can use registers, memory, immediates
MOVSX/MOVZX
  Sign-extend or zero-extend register/memory value
XCHG
  Exchange contents of source, dest

## Slide 8: Review: data transfer, arithmetic
LEA: load effective address
  Calculate EA/store in register
Only flag to worry about: CF
Addition instructions
  ADD AX,BX  AX = AX + BX
  ADC AX,BX  AX = AX + BX + CF
  INC AX  AX = AX + 1
Subtraction instructions
  SUB AX,BX  AX = AX – BX
  SBB AX,BX  AX = AX – BX – CF
  DEC AX  AX = AX – 1
  NEG AX  AX = -AX = 0 - AX

## Slide 9: Review: Multiplication & division
Multiplication instructions
  MUL (unsigned), IMUL (signed)
  Result uses 2x bits of source
  Source usually implied (AL/AX/EAX)
Division instructions
  DIV (unsigned), IDIV (signed)
  Implied source (AX, (DX,AX), (EDX,EAX)) 2x bits of specified source
  Quotient/remainder split across result

## Slide 10: Final notes
Next time:
  Exam 1—PLEASE BE ON TIME!!