## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 20
HLL  assembly

## Slide 2: Announcements/reminders
HW 3 due Monday, 10/21
HW 4 to be posted; due date TBD
Exam 2: Friday, 11/1 in class
  Will again be allowed one note sheet, calculator

## Slide 3: Today’s lecture
Review
  Subroutines
  Basics of stack usage
Translation from HLL  assembly
  Data representations
  Stack accesses
  Array accesses
  Conditional statements
  Loops

## Slide 4: Review: subroutines
Subroutines: low-level functions
  When called, address of next instruction saved
    Return instruction ends routine; goes to that point
  May need to save state on stack
x86 specifics
  CALL <proc>: call procedure
    <proc> can be label (16-/32-bit imm), reg, mem
    Saves address of next instruction to stack
  RET: return from procedure
  Saving state to stack: push instructions
    Store data “above” current TOS; decrement SP
    Basic PUSH stores word or double word
    Directly storing flags: PUSHF
    Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD
  Restoring state: POP/POPF/POPA/POPAD

## Slide 5: HLL  assembly
Given some brief examples already; want to think about common HLL concepts and their assembly counterparts
Compiling HLL to assembly
  Data accesses
  Stack usage with function calls
  Conditional statements (if-then-else)
  Loops

## Slide 6: Sample program
int X[10], Y[10]; // integer arrays
int i, j; // index variables
for (i = 0; i < 10; i++) { // outer loop
X[i] = i * 2; // set X[i]
for (j = 0; j < 10; j++) { // inner loop
if (j < 5) // set Y[j]
Y[j] = X[i] + j; // based on
else // value of j
Y[j] = X[i] – j;
}
}

## Slide 7: Data representations
Program references four pieces of data
  Two integer arrays: X[10], Y[10]
  Two integer index variables: i, j
Compilers must account for:
  Data size: is variable a double word, word, or byte?
    Characters (char) are always 8 bits  1 byte
    Other types system-dependent
      In x86, integers (int) are 32 bits  4 bytes  double word
      Short integers (short) are 16 bits  2 bytes  word
  Data location: where is data allocated?
    Depends on how it’s allocated …
    If writing assembly by hand, static data  directly allocated in memory
    If compiled code or function call, allocated on stack
      Variables declared inside functions, function arguments

## Slide 8: Static data accesses
Global declarations in high-level program
Stored in data segment
Offset into data segment declared as symbol
Example (from testfile2.asm)
  mov eax, DWORD PTR _c

## Slide 9: Stack accesses
On function call
SP or ESP: points to current top of stack
  Lowest address in current stack frame
BP or EBP: used to reference data within frame
  Arguments
  Local variables

## Slide 10: Stack accesses (cont.)
Arguments start at offset 8 from EBP
Local variables start at offset -4 from EBP
Starting offset of each variable can be defined as symbol
Ex. (testfile1.asm) _j$ = -120; size = 4
_i$ = -108; size = 4
_Y$ = -96; size = 40
_X$ = -48; size = 40
mov DWORD PTR _i$[ebp], 0
 sets i = 0

## Slide 11: Array accesses
To access array element, need
  Base address of array
  Offset into array
    Offset = index * (size of each element)
    For example, X[2] is 2*4 = 8 bytes into array X
In some ISAs, need to explicitly calculate this address
  Multiply index by element size
  Add to base address
x86 uses scaled addressing  multiplication done in memory access
  Example: code for X[i] = i * 2 from testfile1:
  mov eax, DWORD PTR _i$[ebp]
  shl eax, 1
  mov ecx, DWORD PTR _i$[ebp]
  mov DWORD PTR _X$[ebp+ecx*4], eax

## Slide 12: Conditional statements
If-then-else statements typically take form similar to:
<code to evaluate condition>
<conditional jump to else if false>
<code if condition true>
jmp end
else: <code if condition false>
end: …
<code to evaluate condition>
  Always requires a conditional branch
  Must add label to branch to “else” statement
Once statement for “if” condition is complete, jump past “else” statement
    Requires insertion of another label for jump target

## Slide 13: Conditional statements (cont.)
Body of inner loop:
if (j < 5)
Y[j] = X[i] + j;
else
Y[j] = X[i] – j;
cmp DWORD PTR _j$[ebp], 5
jge SHORT $LN2@main
mov eax, DWORD PTR _i$[ebp]
mov ecx, DWORD PTR _X$[ebp+eax*4]
add ecx, DWORD PTR _j$[ebp]
mov edx, DWORD PTR _j$[ebp]
mov DWORD PTR _Y$[ebp+edx*4], ecx
jmp SHORT $LN1@main
$LN2@main:
mov eax, DWORD PTR _i$[ebp]
mov ecx, DWORD PTR _X$[ebp+eax*4]
sub ecx, DWORD PTR _j$[ebp]
mov edx, DWORD PTR _j$[ebp]
mov DWORD PTR _Y$[ebp+edx*4], ecx
$LN1@main:

## Slide 14: Loops
For loops are essentially three parts
  Initializing loop index
  Checking boundary condition
    Similar idea to if-then-else statements, but simpler
    If condition is false, end of loop
      Branch to label at first instruction after loop
    Usually done at start of loop, since no iterations should occur unless condition is true
      End of loop then contains jump back to beginning
  Incrementing loop index
While loops only require the boundary condition check

## Slide 15: Loops (cont.)
for (j = 0; j < 10; j++) {// inner loop
mov DWORD PTR _j$[ebp], 0
jmp SHORT $LN5@main
$LN4@main:
mov eax, DWORD PTR _j$[ebp]
add eax, 1
mov DWORD PTR _j$[ebp], eax
$LN5@main:
cmp DWORD PTR _j$[ebp], 10
jge SHORT $LN3@main ; jmp to end
.
. ; Loop body here
.
jmp SHORT $LN4@main
$LN3@main:

## Slide 16: Practice problems
See today’s handout for
  Description of how stack frame should be created
  Description of where to access function arguments, local variables
Functions to be written
  int fact(int n): Calculate and return n!
  int max(int v1, int v2): Return largest value between v1 and v2
  void swap(int *a, int *b): Given addresses a & b, swap contents
Solutions to be posted as PDF online
  C versions in slides that follow; assembly in PDF file
  Will be covered in class today as well

## Slide 17: Factorial in C
int fact(int n) {
int i;
int fact = 1;
for (i = n; i > 1; i--)
fact *= i;
return fact;
}

## Slide 18: Maximum value function in C
int max(int v1, int v2) {
if (v1 > v2)
return v1;
else
return v2;
}

## Slide 19: Swap in C
void swap(int *a, int *b) {
int temp;
temp = *a;
*a = *b;
*b = temp;
}

## Slide 20: Final notes
Next set of lectures: PIC microcontrollers and ISA
Reminders:
  HW 3 due Monday, 10/21
  HW 4 to be posted; due date TBD
  Exam 2: Friday, 11/1 in class
    Will again be allowed one note sheet, calculator