## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors:
Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 24
Exam 2 Preview

## Slide 2: Lecture outline
Announcements/reminders:
  HW 4 due today—no late submissions accepted
Today’s lecture: Exam 2 Preview

## Slide 3: Exam 2 notes
Please attend your registered section unless you have permission to do otherwise
Allowed
  One 8.5” x 11” double-sided sheet of notes
  Calculator
No other notes or electronic devices
Exam will last 50 minutes
Covers lectures 12-13, 15-23
Format similar to old exams
  1 multiple choice question (instructions covered)
  1 short code sequence to evaluate (logical/shift/rotate/bit scan)
  1 set of short answer questions
  2 short instruction sequences to write

## Slide 4: Review: Logical instructions
Logical instructions (AND/OR/XOR/NOT)
Basic shift instructions
  Move value by <amt> bits; add 0s to left or right
  CF = last bit shifted out
  SHL <src>, <amt>: Move <src> to left
    SAL exactly the same
  SHR <src>, <amt>: Move <src> to right
Arithmetic right shift
  Move value right by <amt> bits
  Copy sign bit to fill remaining bits
  CF = last bit shifted out
  SAR <src>, <amt>

## Slide 5: Review: rotate instructions
Rotate instructions: bits that are shifted out one side are shifted back in other side
  ROL <src>, <amt> or ROR <src>, <amt>
  CF = last bit rotated
Rotate through carry instructions
  CF acts as “extra” bit that is part of value being rotated
  RCL <src>, <amt> or RCR <src>, <amt>

## Slide 6: Review: bit test/scan instructions
BT  Bit test
BTR  Bit test and reset (source bit = 0)
BTS  Bit test and set (source bit = 1)
BTC  Bit test and complement (flip source bit)
Examples
  BT AX, 0  CF = bit 0 of AX
  BTC BX, 3  CF = bit 3 of BX; flip bit 3 of BX
BSF  Bit scan forward (start with bit 0)
BSR  Bit scan reverse (start with bit 1)
Example:
  BSF ESI,EDX  32-bits of EDX scanned starting from B0
  If EDX = 0x00000000  ZF = 0 (all bits zero)
  If EDX = 0x00000001  ESI = 0x00000000, ZF = 1 (bit 0 is 1)
  If EDX = 0x00003000  ESI = 0x0000000C, ZF = 1 (bit 12 is first bit set to 1)

## Slide 7: Review: compare
CMP D, S
  Flags show result of (D) – (S)
Condition codes: mnemonics implying certain flag conditions

## Slide 8: Review: conditional instructions
Conditional move
  Move performed only if condition is true
SETcc D
  Sets single byte destination to 1 (0x01) if condition true; all 0s (0x00) if condition false
  Can be used to build up complex conditions

## Slide 9: Review: jump, loop
Two general types of jump
  Unconditional: JMP <target>
    Always go to target address
  Conditional: Jcc <target>
    Go to target address if condition true
Loop instructions
  Combines CX decrement with JNZ test
  May add additional required condition
    LOOPE/LOOPZ: loop if ((CX != 0) && (ZF == 1))
    LOOPNE/LOOPNZ: loop if (CX != 0) && (ZF == 0))

## Slide 10: Review: subroutines
Subroutines: low-level functions
  When called, address of next instruction saved
    Return instruction ends routine; goes to that point
  May need to save state on stack
x86 specifics
  CALL <proc>: call procedure
    <proc> is written as label
  RET: return from procedure
  Saving state to stack: push instructions
    Store data “above” current TOS; decrement SP
    Basic PUSH stores word or double word
    Directly storing flags: PUSHF
    Storing all 16-/32-bit general purpose registers: PUSHA/PUSHAD
  Restoring state: POP/POPF/POPA/POPAD

## Slide 11: Review: HLL  assembly
Data accesses
  Global variables  static; allocated in data segment
  Other variables  dynamic; allocated on stack
  Stack frame for each function contains (from top)
    Saved variables within function
    Local variables for function (starting at EBP – 4)
    Saved EBP
    Saved EIP
    Function arguments (starting at EBP + 8)
Conditional statements (if-then-else)
  Evaluate condition (CMP instruction(s))
  Conditional jump (often to “else” case)
  “If” case ends with unconditional jump to skip “else”
Loops
  Initialize variable at start
  Test loop condition (similar to if)
  Change loop variable

## Slide 12: Review: Stack accesses
On function call
SP or ESP: points to current top of stack
  Lowest address in current stack frame
BP or EBP: used to reference data within frame
  Arguments
  Local variables

## Slide 13: Review: Stack accesses (cont.)
Arguments start at offset 8 from EBP
Local variables start at offset -4 from EBP
Starting offset of each variable can be defined as symbol
Ex. (testfile1.asm) _j$ = -120; size = 4
_i$ = -108; size = 4
_Y$ = -96; size = 40
_X$ = -48; size = 40
mov DWORD PTR _i$[ebp], 0
 sets i = 0

## Slide 14: Final notes
Next time:
  Exam 2—PLEASE BE ON TIME
Reminders
  HW 4 due today—no late submissions accepted