## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructors: Dr. Lin Li & Dr. Michael Geiger
Fall 2019
Lecture 34:
Continue with PIC example programs:
Working with delay

## Slide 2: Lecture outline
Review: working with PICkit
  Assembler/MPLAB basics
  Use of MPLAB IDE
Today’s lecture: different ways of managing delay
  Instruction count-based delay loop
  Timer-based delay loop

## Slide 3: Review: PIC assembler/MPLAB basics
Selecting bank of particular register:
banksel label
Defining starting address of code:
org address
Definitions added with: #include file
Basic configuration setup: Window  PIC Memory Views  Configuration Bits
  Can set bits one by one, then generate code to paste into your program

## Slide 4: Review: Running PIC programs
Choose target device under
File  Project Properties
  Either use PICkit3 or Simulator
Compilation
  Clean and Build
  Make and Program Device (PICkit3 only)
    Separate options required for debug configuration
    Click arrow on right of button to build/make for debug
Window  PIC Memory Views
  Allows you to view file registers and/or SFRs

## Slide 5: Example: Blink LED (.asm) (1 of 2)
cblock 0x70 ;shared memory accessible from all banks
Delay1 ;Two registers for delay loop in shared mem
Delay2
endc
ORG 0
Start:
banksel OSCCON ;bank1
movlw b'00111000' ;set cpu speed of 500KHz
movwf OSCCON ;OSCCON configures
; internal clock
bcf TRISC,0 ;Pin C0 = output for DS1
banksel LATC ;bank2
clrf LATC ;Turn off all of the LEDs

## Slide 6: Example 2: Blink LED (.asm) (2 of 2)
MainLoop:
bsf LATC, 0 ;turn on DS1
OndelayLoop:
decfsz Delay1,f ;Waste time.
bra OndelayLoop ;Inner loop takes 3 instructions
; per loop * 256 loops = 768 instructions
decfsz Delay2,f ;The outer loop takes an additional 3
; instructions per loopp * 256 loops
bra OndelayLoop ;(768+3) * 256 = 197376 instructions /
; 125K instructions per second =
; 1.579 sec.
bcf LATC,0 ;Turn off LED C0
OffDelayLoop:
decfsz Delay1,f ;same delay as above
bra OffDelayLoop
decfsz Delay2,f
bra OffDelayLoop
bra MainLoop ;Do it again...
end

## Slide 7: Example 2: Blink LED (C)
void main(void) {
unsigned int delay; // 16 bit variable
OSCCON = 0b00111000; //500KHz clock speed
TRISCbits.TRISC0 = 0; //using pin as output
delay = 11250;
while (1) {
//each instruction is 8us (1/(500KHz/4))
while(delay-- != 0)continue;
LATCbits.LATC0 ^= 1; //toggle LED
delay = 11250; //reset delay counter
}
}

## Slide 8: Oscillator module
Configurable oscillators to determine controller speed
Internal or external oscillator
Multiple scalable internal clocks
  Low frequency: 31 kHz
  Medium frequency: 500 kHz
  High frequency: 16 MHz
    Generated from medium frequency
  Low and medium can be divided to produce frequencies from 16 MHz to 31.25 kHz
Clock selected using appropriate bits in OSCCON register

## Slide 9: “Simplified diagram” of clock sources

## Slide 10: Rotate LEDs with delay loop (asm)
Start:
banksel OSCCON ;bank1
movlw b'00111000' ;set cpu clock speed of 500KHz
movwf OSCCON
clrf TRISC ;make all of PORTC an output
banksel LATC ;select the bank where LATC is (bank2)
movlw b'00001000' ;start the rotation by setting DS4 ON
movwf LATC
MainLoop:
OndelayLoop:
decfsz Delay1,f ;Delay loop ~ 1.5 s
goto OndelayLoop
decfsz Delay2,f
goto OndelayLoop
Rotate:
lsrf LATC,F ;shift LEDs & turn on LED to the right
btfsc STATUS,C ;Is carry 1? (was DS1 just lit?)
bsf LATC, 3 ;if so, start the sequence over again
goto MainLoop
end ;end code section

## Slide 11: Rotate LEDs with delay loop (C)
void main(void) {
TRISC = 0; //all pins are outputs
OSCCON = 0b00111000; //500KHz clock speed
LATC = 0b0001000; //start rotation by setting
//DS4 ON - rotate from the right to left
while (1) {
__delay_ms(500); //delay 500ms
LATC >> = 1; //shift to the right by 1
// When last LED is lit, restart pattern
if(STATUSbits.C)
LATCbits.LATC3 = 1;
}
}

## Slide 12: Timer module
Internal timers common in microcontrollers
Used to generate delays, measure time between events, or count event occurrences
Typical interrupts for
  Timer overflow (common for generating delay)
  Timer compare (also for generating delay—stop when timer reaches certain value)
  Capture (what value does timer have when event occurs?)
Typical timer configurations
  Run at particular speed relative to system clock (prescaled)
  Increment every time external event occurs
PIC 16F1829 has 5 timers (four 8 bit, one 16 bit)

## Slide 13: Rotate with timer-based delay (asm) (1/2)
Start:
;Setup main init
banksel OSCCON ;bank1
movlw b'00111000’ ;set cpu clock speed to 500KHz
movwf OSCCON
;Configure the LEDs
banksel TRISC ;bank1
clrf TRISC ;make all of PORTC an output
banksel LATC ;bank2
movlw b'00001000‘ ;start with DS4 lit
movwf LATC
;Setup Timer0
banksel OPTION_REG ;bank1
;1:256 prescaler for a delay of:
; (insruction-cycle * 256-counts)*prescaler =
; ((8uS * 256)*256) =~ 524mS
movlw b'00000111’
movwf OPTION_REG

## Slide 14: Rotate with timer-based delay (asm) (2/2)
MainLoop:
btfss INTCON, TMR0IF ;did TMR0 roll over yet?
bra $-1 ;wait until TMR0 overflows
bcf INTCON, TMR0IF ;clear flag in software
;rotate the LEDs
banksel LATC ;bank2
lsrf LATC, f
btfsc STATUS,C ;did bit rotate into carry?
bsf LATC,3 ;yes, light DS4 back up
bra MainLoop ;continue forever
end

## Slide 15: Rotate with timer-based delay (C)
void main(void) {
OSCCON = 0b00111000; //500KHz clock speed
TRISC = 0; //all LED pins are outputs
LATC = 0;
//1:256 prescaler for a delay of: (instruction-cycle * 256
// counts)*prescaler = ((8uS * 256)*256) =~ 524mS
OPTION_REG = 0b00000111;
LATCbits.LATC4 = 1; //start with DS4 lit
while (1) {
//PIC can do work here, but this program just waits for flag
while (!INTCONbits.TMR0IF) continue;
INTCONbits.T0IF = 0; //flag MUST be cleared in software
LATC >> = 1; //rotate the LEDs
if (STATUSbits.C) //when last LED is lit, restart pattern
LATCbits.LATC3 = 1;
}
}

## Slide 16: Final notes
Next time:
  PIC interrupts