## Slide 1: EECE.3170 Microprocessor Systems Design I
Instructor: Dr. Michael Geiger
Summer 2017
Lecture 1:
Course overview
Role of ISA
Data types, storage, and addressing

## Slide 2: Lecture outline
Announcements
  HW 1 due 1:00 PM, 5/18
  Exam 3: 6/22 instead of 6/26?
Lecture outline
  Course overview
  General microprocessor introduction
  Role of the instruction set architecture
  Data types
  Data storage and addressing

## Slide 3: Course meeting times
Lectures:
  Section 011: MWTh 10:30-12:50, Falmouth 205
Lab: Not required; will get access to Ball 424 if necessary

## Slide 4: Course instructors
Instructor: Dr. Michael Geiger
  E-mail: Michael_Geiger@uml.edu
  Phone: 978-934-3618 (x43618 on campus)
  Office: 118A Perry Hall / 301A Ball Hall (as of 5/24)
  Office hours: TBD
    Most likely: stick around to answer questions right after lecture
    Available by appointment at other times

## Slide 5: Course materials
Textbook: None
  Will post relevant online resources on schedule page
Course website: http://mjgeiger.github.io/eece3170/sum17/index.htm
  Will contain lecture slides, handouts, assignments
Discussion group through piazza.com
  Allow common questions to be answered for everyone
  All course announcements will be posted here
  Will use as class mailing list—please enroll ASAP

## Slide 6: Additional course policies
Prerequisites
  EECE.2160 (ECE Application Programming)
  EECE.2650 (Logic Design)
Assignments
  Homework, labs, and some “hybrid” assignments (problems + programming exercise(s))
  Late assignments: 10% penalty per day
  All HW individual unless otherwise specified
  Some assignments require instructor “check-off”

## Slide 7: Academic honesty
All assignments are to be done individually unless explicitly specified otherwise by the instructor
Any copied solutions, whether from another student or an outside source, are subject to penalty
You may discuss general topics or help one another with specific errors, but not share assignment solutions
  Must acknowledge assistance from classmate in submission

## Slide 8: Course “rules”
A couple of unofficial rules:
Please call me “Dr. Geiger”
  “Professor Geiger” is okay (although I’m technically not a professor, I’m a lecturer)
  “Michael,” “Mike,” or “Geiger” is not okay
Please don’t talk when I’m talking
  Doing so distracts your classmates and me
  If you have a question, please raise your hand and ask—I want questions during lecture!

## Slide 9: Course policies (cont.)
Grading breakdown
  Assignments: 55%
  Exam 1: 15%
  Exam 2: 15%
  Exam 3: 15%
Exam dates
  Exam 1: Thursday, May 25 in class
  Exam 2: Monday, June 12 in class
  Exam 3: Thursday, June 22 (preferred) -or- Monday, June 26

## Slide 10: What you should learn in this class
Two major aspects:
  How to program
    Focus on assembly language
    Will look at HLL  assembly translation, integration
    Use of HLL with microcontrollers
  How a microprocessor works with other components
    Focus on interfacing circuits and control schemes
Will work with two processor families:
  Intel x86 architecture  assembly language simulation
  PIC microcontroller  actual microcontroller programming, interfacing
· To understand the interconnection of the CPU, memory, and I/O

## Slide 11: Tentative course outline
General microprocessor introduction
Assembly language programming
  Start with x86; introduce PIC microcontroller about halfway
  Areas will include
    Addressing modes
    Instruction types
    Programming modes
    HLL and assembly—translation; combination
External interfacing
  Processor signals used in interfacing
  Interface circuitry
  External memory
Interrupts
Microcontroller-based systems
  Microcontrollers vs. microprocessors
  Design of microcontroller-based circuits
  High-level programming of microcontrollers

## Slide 12: What is a computer?
From The American Heritage Dictionary:
  “One who computes”
    We could argue that people are computers
  “A device that computes, especially a programmable electronic machine that performs high-speed mathematical or logical operations or that assembles, stores, correlates, or otherwise processes information.”
    Anything from a simple abacus to the microprocessor-based computers of today

## Slide 13: Computing history
The first electronic digital computer – ENIAC, built in UPenn in 1946
Thirty tons
Forced air cooling
200KW
19,000 vacuum tubes
Punch card
Manual wiring
Numerical computation
Source: http://ei.cs.vt.edu/~history/ENIAC.Richey.HTML

## Slide 14: Today’s computer: one example
iPhone 6s Technical Specifications
(the 6s Plus wouldn’t fit on the slide)
Screen size 4.7 inches
Screen resolution 1334 by 750 at 326 ppi
Input method Multi-touch
Operating system iOS 9.3.1
Storage 16 / 64 / 128 GB
Cellular network UMTS/GSM/CDMA
Wireless data Wi-Fi (802.11a/b/g/n/ac) +
LTE + Bluetooth 4.2 + NFC
Camera 12.0 megapixels
Battery Up to 11 hrs Internet,
14 hrs talk,
11 hrs video, 50 hrs audio,
10 days standby
Dimensions 5.44 x 2.64 x 0.28 inches
Weight 5.04 ounces
Source: http://www.apple.com/iphone-6s/specs/

## Slide 15: Processor market (as of 2007)
“Computer” used to just refer to PCs
Processors—and, therefore, computers—are now everywhere

## Slide 16: Computer components
What are the key components of a computer?
  Microprocessor (MPU/CPU) performs computation
  Input to read data from external devices
    Examples: Keyboard, mouse, ports (Ethernet, USB, etc.)
  Output to transmit data to external devices
    Examples: screen, speaker, VGA interface, ports (Ethernet, USB, etc.)
  Storage to hold program code and data
    RAM, hard disk, possibly other media (CD/DVD, external drive)
  Power supply
Will see that microprocessor contains smaller-scale versions of these components
  Computation engine
  I/O interface
  Internal storage

## Slide 17: Processor architecture
“Architecture” can refer to
  High-level description of hardware; could be
    Overall system
    Microprocessor
    Subsystem within processor
  Operations available to programmer
    Instruction set architecture
  Other applications to computing (e.g., “software architecture”) we won’t discuss
Commonly used to discuss functional units and how they work together

## Slide 18: Role of the ISA
User writes high-level language (HLL) program
Compiler converts HLL program into assembly for the particular instruction set architecture (ISA)
Assembler converts assembly into machine language (bits) for that ISA
Resulting machine language program is loaded into memory and run

## Slide 19: Abstraction of program control
Easiest for humans to understand high-level languages
Processor interprets machine language
Assembly language: abstraction with intermediate level of detail
  Breaks machine code into instructions
  Gives some insight into how each instruction behaves
  More readable than bit patterns!

## Slide 20: ISA design
Think about a HLL statement like
X[i] = i * 2;
ISA defines how such statements are translated to machine code
  What information is needed?

## Slide 21: ISA design (cont.)
Think about a HLL statement like
X[i] = i * 2;
Questions answered in every ISA (or “software model”)
  How will the processor implement this statement?
    What operations are available?
    How many operands does each instruction use?
  Where are X[i] and i?
    How do we reference the operands?
  What type(s) of data are X[i] and i?
    What types of operands are supported?
    How big are those operands?
  Instruction format issues
    How many bits per instruction?
    What does each bit or set of bits represent?
    Are all instructions the same length?

## Slide 22: Operation types
Operations: what should processor be able to do?
  Data transfer
    Move data between storage locations
  Arithmetic operations
    Typical: add, subtract, maybe multiply/divide, negation
  Logical operations
    Typical: AND, OR, NOT, XOR
    Often includes bit manipulation: shifts, rotates, test/set/clear single bit
  Program control
    “Jump” to another part of program
    May be based on condition
    Used to implement loops, conditionals, function call/return
  Typically some processor-specific special purpose ops

## Slide 23: Operands
Two major questions when dealing with data
  “How” do we store them?  what do the bits represent?
  Where do we store them?
    … and how do we access those locations?
First question deals with data types
Second question deals with data storage and addressing

## Slide 24: Data types
Also seen in high-level languages
  Think about C types: int, double, char, etc.
  What does a data type specify?
    How big is each piece of data?
    How do we interpret the bits representing those data?
Data sizes
  Smallest addressable unit: byte (8 bits)
  Can also deal with multi-byte data: 16, 32, 64 bits
  Often deal with words of data
    Word size processor-dependent (16 bits on x86, 32 bits on MIPS)
    Can have double words, quad words, half words …
Interpreting bits
  Numbers: Integers, floating-point; signed vs. unsigned
  May treat as characters, other special formats

## Slide 25: Unsigned Integers
Types:
Sizes Range
8-bit 0H  25510
16-bit 0H  65,53510
32-bit 0H  4,294,967,29510

## Slide 26: Signed Integers
MSB is sign bit ( 0/1 -> +/-)
Remaining bits represent value
Negative numbers expressed in 2’s complement notation
Types:
Sizes Range
8-bit -128  +127
16-bit -32,768  +32,767
32-bit -2,147,483,648  +2,147,483,647

## Slide 27: Integer Examples
Given the 8-bit value: 1001 11112
Calculate the decimal value of this integer as
  An unsigned integer
  A signed integer

## Slide 28: Integer example solution
Given the 8-bit value: 1001 11112
Calculate the decimal value of this integer as
  An unsigned integer
  Solution:
    (1 x 27) + (1 x 24) + (1 x 23) + (1 x 22) + (1 x 21) + (1 x 20)
    = 128 + 16 + 8 + 4 + 2 + 1 = 159
  A signed integer
  Solution:
    MSB = 1  negative value
    To get magnitude, take 2’s complement:
    0110 00012 = (1 x 26) + (1 x 25) + (1 x 20)
    = 64 + 32 + 1 = 97
     Result = -97

## Slide 29: BCD Numbers
Direct coding of numbers as binary coded decimal (BCD) numbers supported
Unpacked BCD [Fig.2.10(b)]
  Lower four bits contain a digit of a BCD number
  Upper four bits filled with zeros (zero filled)
Packed BCD [Fig. 2.10(c)]
  Lower significant BCD digit held in lower 4 bits of byte
  More significant BCD digit held in upper 4 bits of byte
Example: Packed BCD byte at address 01000H is 100100012, what is the decimal number?
Organizing as BCD digits gives,
1001BCD 0001BCD = 9110

## Slide 30: ASCII Data
American Code for Information Interchange (ASCII) code
ASCII information storage in memory
  Coded one character per byte
  7 LS-bits = b7b6b5b4b3b2b1
  MS-bit filled with 0
Example: Addresses 01100H-01104H contain ASCII coded data 01000001, 01010011, 01000011, 01001001, and 01001001, respectively. What does the data stand for?
0 100 0001ASCII = A
0 101 0011ASCI = S
0 100 0011ASCII = C
0 100 1001ASCII = I
0 100 1001ASCII = I

## Slide 31: Real Numbers
Floating-point data stored in two parts
  Significand (fraction)
  Exponent
Single-precision (32 bits) or double-precision (64 bits)

## Slide 32: Data storage
What characteristics do we want storage media to have?
Two primary answers
  Speed
  Capacity
  Very difficult to get both in single storage unit
Processors use two different types of storage
  Registers
  Memory

## Slide 33: Registers
Small, fast set of storage locations close to processor core (execution engine)
Primarily used for computation, short-term storage
  Speed  ideal for individual operations
  Lack of capacity  will frequently overwrite
Reference registers by name
  Example: ADD EAX, EBX  EAX = EAX + EBX
  EAX, EBX are registers in x86 architecture

## Slide 34: Memory
Provides enough capacity for all code, data (possibly I/O as well)
Typically organized as hierarchy
Used primarily for long-term storage
  Lacks speed of registers
  Provides capacity to ensure data not overwritten
Reference memory by address
  Example: MOV EAX, [100h]
   EAX = memory at address [100h]

## Slide 35: Memory (continued)
Accessing single byte is easy
Considerations with multi-byte data
  Are the data aligned?
    Easier/faster to access aligned data
  How are the data organized in memory (“endianness”)?
    Given 32-bit number: DEADBEEFh or 0xDEADBEEF
    Which byte—MSB (0xDE) or LSB (0xEF) gets stored in memory first?

## Slide 36: Aligned Words, Double words
Aligned data: address is divisible by # of bytes
  2 bytes  address must be even
  4 bytes  address must be multiple of 4
x86 architecture doesn’t require aligned data access
  Performance impact for accessing unaligned data in memory (32-bit data bus)
Byte address |  |  |  |  | 
0 |  |  |  |  | 
4 |  |  |  |  | 
8 |  |  |  |  | 
12 |  |  |  |  | 
16 |  |  |  |  | 
20 |  |  |  |  | 
Aligned word
Aligned double word
Unaligned
word
Unaligned
double
word

## Slide 37: Byte order (“endianness”)
In a multi-byte operand, how are the bytes ordered in memory?
Assume the double word value 1,000,000 (0x000F4240) is stored at address 80
  In a little-endian ISA (like x86), the least significant byte (the “little” end) is at address 80
  In a big-endian ISA (like MIPS), it’s the other way around
 |  | 00 | 0F | 42 | 40 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …
 |  | 40 | 42 | 0F | 00 |  | 
… | 79 | 80 | 81 | 82 | 83 | 84 | …

## Slide 38: Examples
Given the following memory contents:
  Starting address of each line shown on left
  Leftmost byte has lowest address
    First line: addresses 0x200C, 0x200D, 0x200E, 0x200F
What is the value of:
  The word starting at address 0x200D?
  The double word starting at address 0x2012?
Are these data aligned?
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 39: Solution
Word at 0x200D = 0x2C96
  Address is not divisible by 2  unaligned
Double word at 0x2012 = 0x2301ABCD
  Address is not divisible by 4  unaligned
    Remember, hexadecimal is base 16—0x12 = 1810
 | Lo |  |  | Hi
0x200C | 40 | 96 | 2C | 00
0x2010 | 55 | 12 | CD | AB
0x2014 | 01 | 23 | 88 | 99

## Slide 40: Final notes
Next time:
  x86 introduction
  Assembly basics
  Data transfer instructions
Reminders:
  HW 1 due 1:00 PM, 5/18
  Sign up for the discussion group on Piazza